##### Raytheon

## UNITED STATES ANTARCTIC PROGRAM

## National Science Foundation

## Contract OPP 0000373

## MODIS Data in the USAP

###### Use of the McMurdo MGS for MODIS data collection

## Raytheon Technical Services Company

Polar Services

61 Inverness Drive East

#### Suite 300

Englewood, Colorado

80112 USA

303.790.8606

# History

The Terra satellite successfully launched from Vandenberg Air Force Base on Saturday, December 18, 1999 at 18:57 GMT.  This satellite was the first of NASA’s Earth Observing System (EOS) series to carry the Moderate-resolution Imaging Spectroradiometer (MODIS) sensor package. MODIS has been measuring visible and infrared wavelengths from all over our world at multiple scales of time and space since February 2000. MODIS extends the measurements begun by CZCS and AVHRR, and now provides improvements in spectral detail, spatial resolution and accuracy over previous sensors.  MODIS data products from Terra have been available since February of 2000. MODIS' data products are available at spatial resolutions ranging from 250 m per pixel, to 1 km, to 1 degree.  Multiple passes of the satellite occur every day.  Other sensors on Terra include ASTER, or Advanced Spaceborne Thermal Emission and Reflection Radiometer, CERES, or Clouds and Earth's Radiant Energy System, MISR, or Multi-angle Imaging Spectroradiometer, and MOPITT, or Measurements of Pollution in the Troposphere.  Terra will be joined by Aqua, the next in the EOS satellite series, with a scheduled launch of March 2002.  Data products are anticipated to be available from Aqua within 150 days of becoming operational.

# Proposal

At the request of the National Science Foundation’s office of Polar Programs, a discussion was initiated between the National Science Foundation (NSF), NASA, and Raytheon Polar Services (RPSC) on the feasibility of acquiring MODIC data from Terra and Aqua using the 10-meter main ground station (MGS) at McMurdo Station in Antarctica.  NASA and the NSF operate the MGS under a Memorandum of Agreement for RadarSat data collection and other, as needed satellite communications at McMurdo.  NASA provides a portion of on-ice operations and management cost, as well as providing on-ice labor, which is reimbursed by the NSF.  David Bromwich from the Byrd Research Center was contacted by RPSC to establish the constraints on data acquisition necessary to achieve their research goals using MODIS data.  It was determined that 3 consecutive passes of the satellite were needed each day to provide the required time series.  Independent analysis of the orbital data for Terra and RadarSat showed a potential conflict once every four days.  David Bromwich affirmed that a one-day gap every 4 days in data collection for MODIS data would be acceptable.  Researchers Dan Lubin and Matthew Lazzara have provided observations pertinent to their research communities.  Please see Appendix B and Appendix C.

# Design

The following designs were studied in the course of three joint teleconferences:

- Receive the data through the MGS and use the NASA system to process the data to level 0 files, and place a computer with a DLT tape drive in the MGS facility to write this data to tape

- Receive the data through the MGS and use the NASA system to process the data to level 0 files, then ftp this data across the network to another facility with a computer which could write the data to DLT tape

- Receive the signal with the MGS antenna and use an IF feed from the MGS over fiber to a SeaSpace Terascan system at another location for processing to a level 0 file and output to DLT tape.

Design 1 was rejected due to the need to have staff onsite at the MGS to perform the necessary processing and tape generation.  Design 2 was rejected due to the need to send Gigabyte files over a branch of the network running on a 10 Mbps Ethernet link which is already carrying RadarSat traffic.  The decision was made to go with design 3.  This design requires:

- An IF amplifier or matrix switch to provide an additional IF feed off of the NASA MGS

- A transceiver to put this 375 MHz IF signal on single mode fiber

- Single mode fiber run from the MGS facility to the processing facility

- A transceiver converting from fiber back to the IF signal

- A SeaSpace TeraScan system to ingest and process that signal through an up-converter to their standard 750 MHz IF signal.

We have identified the following fiber runs as being available:

- Between MGS and Crary Lab room 205:  8 of 12 sm fibers are available

- Between MGS and B-140: 10 of 12 sm fibers are available 8 need, connectors installed

# Initial Costs

- IF amplifier and spare							$   1,000

- IF Fiber Link transceiver set, rackmount, and spares			$   6,300

- Terascan system with 375 MHz upconverter (spares already on-site)	$129,000

- SeaSpace training course – required for warranty				$   4,000

- Installation labor – RPSC						$   5,000

- Travel – RPSC for installation						$   4,000

- SeaSpace engineer visit (optional – could be done remotely)		$  10,575

- Recommended spares	(note: receiver is unique to X-Band)		$  76,049

Total		$235,924

# Outyear Costs

- SeaSpace software annual license fee					$  4,000

# Operational Impacts

The only significant operational impacts are the additional tasking of IT staff to monitor and maintain the system and change DLT tapes as needed, the shipping of those tapes back to CONUS, and distribution of the tapes to the data repository.

# Appendix A – Minutes from the October MODIS Teleconference

Continuing Discussion on MODIS Data Collection using MGS at McMurdo

Conference attendees representing NASA, NSF, SeaSpace, and RPSC

Discussion on data collection constraints for user community:

It was brought up at the last meeting that conflicts with RadarSat data collection

might prevent MODIS data collection one day every 4 days.  Discussions with

David Bromwich at Byrd Research indicated that this would not be a problem, and

3 consecutive days of 3 consecutive passes each day would be adequate.

Discussion on whether to process files in the NASA VCDU locally and then transfer to town via network, or use fiber to transfer Intermediate Frequency signals to an ingest Terascan in town.

The MGS is on a 10 megabit Ethernet line, and traffic considerations would prohibit

transferring gigabit data files via the network.  The NSF has requested that the IF

be fed to town using existing dark fiber at the ground station.  SeaSpace has

the ability to add an upconverter to the Terascan receiver to convert the NASA

375 MHz IF to the expected 720 MHz.

It was pointed out that the only extra IF output on the MGS is a spare, and might

be needed at some point.  NASA suggested an IF amplifier permitting multiple

outputs from the existing feed.  NSF suggested a small RF matrix switch might

also serve for distribution.

It was determined that the system would not be installed earlier than 11/01/02.

Action Items:

NASA:		(due 11/01/01)

Dennis Mateik is to perform a scheduling analysis for MODIS data collection,

showing any conflicts with RadarSat and ERS, other backup collection, and

other routine collection.

Dennis Mateik is to determine whether this MODIS activity would be within

the scope of the existing agreement between NASA and the NSF, or how

much additional costs would be incurred.

All results to be provided to Dave Leger at RPSC for reporting.

SeaSpace:	(due 10/25/01)

Buzz Bernstein is to produce a quote for a Terascan system, minus antenna

systems, with the appropriate 375 MHz to 720 MHz upconverter.  Quote to

be provided to Dave Leger at RPSC.

RPSC: 		(due 11/15/01)

RPSC will determine components and costs for sending the 375 MHz IF

signal from the MGS to town via transceivers and fiber, including any IF amp or

matrix switch at the MGS end, and any line level adjuster at the town end.  This

IF work is to be coordinated with Buzz Bernstein of SeaSpace for the town end

and Dave Hess of CSOC - Wallops for the MGS end.

RPSC will consolidate materials from NASA and SeaSpace, as well as the IF

design and pricing, and deliver the consolidated report to the NSF.

# Appendix B – Comments on Research Impacts by Dan Lubin

General comments:

1. If we're looking at a potential RadarSat interruption only once every four

days, and the system is free to schedule passes on most of that interrupted day

and most of the time the other days, I don't think there is a fundamental

conflict with researcher support objectives, provided the scheduling of passes

is under scientific supervision.  The RadarSat is a 5:30 PM spacecraft, while

Terra and Aqua are 10:30 and 1:30 equator crossing spacecraft, respectively.

2. Matt and Chuck at SSEC can speak more clearly about the meteorological

support objectives, but from my understanding: (a) MODIS-derived winds require

at least 3 consecutive passes per day (preferably twice that, because 3 passes

only gives you one wind field per day), and (b) MODIS-based fog detection

requires the most recent pass available.  David Bromwich has already stated his

minimum requirement of 3 consecutive daily passes.

3. High resolution mapping of sea ice for research support requires one

clear-sky look per day, but due to prevalent cloud cover will usually require

several passes per day to have a chance at a clear-sky look.

4. The Indian Oceansat Ocean Color Monitor (OCM) is a value added MODIS-like

instrument that is easily acquired by the SeaSpace system.  It is valuable for

weather observation, sea-ice support, and as a high-resolution supplement to

SeaWiFS chlorophyll data products.  This is a 12:00 noon spacecraft, and some

flexibility should be preserved for tracking Oceansat passes.

[ Dan Lubin goes on to say that with adequate antenna scheduling and access, science support objectives should not be seriously compromised, but that a dedicated MODIS ground station would offer more flexibility.  He anticipates additional requests for MODIS data by researchers, once it is available on the ice.]

Specific Research Comments:

My own satellite research has involved remote sensing of clouds for

understanding climate and radiation balance, for UV ecological studies, and has

also involved enhancements to sea ice remote sensing capabilities.  Over the

years, these efforts have been supported by OPP, by NSF Climate Dynamics, and by

NASA.  Close coordination with fieldwork has been very important in my research

over the years.  In order of priority, I would like to see from an X-band system:

1. 3 consecutive passes from Terra MODIS.  When Aqua is up (scheduled for March,

2002), an additional 3 consecutive passes from Aqua MODIS. These should be

during the best daylight hours in the sunlit part of the year.  In winter,

there's more flexibility with scheduling.

(note that this implies occasional mid-day pass scheduling conflicts

between Terra and Aqua.)

2. The above should be mostly adequate for sea ice work once Aqua is up, but

could be supplemented by 1 - 2 Oceansat OCM images per day.

3. When experimental programs are in the field, either my own or those of

collaborators such as Prof. Von Walden (U. Idaho), the flexibility to schedule

1-2 extra MODIS passes per day to coincide with specific data collection

activities (e.g., a spectral radiometer measurement or an in situ atmospheric

measurement).

# Appendix C – Comments on Additional Applications by Matthew Lazzara

1.  With the generation of our Antarctic composite images, it would be

ideal to get images that would go with each of the 8 images we generate

each day (at 0, 3, 6, 9, 12, 15, 18, and 21 UTC).  I realize that this is

unlikely on the fairly tasked existing X-band system. However, it would be

ideal. Also, this item would require real-time access to the data.

2.  The iceberg monitoring activities wouldn't need more than the 2 or 3

images per day, and of course, real-time access have been very valuable for

NSF-OPP ops as well as those of us researching this.

3. I would like to ask that the data be archived in the HDF-EOS (Terra's

"level 1b") format.  This is the NASA standard format of the data, and

could be used more widely by more users.

# Appendix D – SeaSpace System Quote