The Future of the Next Generation Satellite Fleet and the McMurdo Ground Station

A Report to the

Office of Polar Programs

National Science Foundation

United States Antarctic Program

Edited by

Matthew A. Lazzara and Charles R. Stearns

Antarctic Meteorological Research Center

Space Science and Engineering Center

University of Wisconsin-Madison

#### May 31, 2004

Funded by NSF-OPP Grant #OPP-0412586

University of Wisconsin-Madison, Space Science and Engineering Center

Publication #

Photo by Pat Smith, NSF-OPP

Table of Contents

Executive Summary	3

Introduction and Background	4

The McMurdo Ground Station (MGS)	4

McMurdo Station Meteorological Satellite Direct Readout History	8

Communications	8

Present Status	8

Future Requirements	9

Short Term	9

Mid Term	9

Long Term	10

Science and Operational Requirements	11

Scope and Effects	11

Multi-discipline Benefits	11

Impacts	12

Implementation	12

Short Term	13

Mid Term	13

Long Term	14

Limiting Factors	15

Communications	16

Closed Network	16

McMurdo TDRSS Relay System (MTRS)	16

Infrastructure	16

Conclusions and Recommendations	18

Acknowledgements	19

References	20

Appendices	22

Web sites	22

Acronyms	23

NPOESS Sensors and Capabilities	25

Workshop Attendees	28

# Executive Summary

The purpose of this report is to provide information, options, and recommendations for deciding how to collect the transmitted data from the next generation of polar orbiting satellites for use by the United States Antarctic Program (USAP) in Antarctica. X-band direct broadcast satellites are replacing the L-band direct broadcast satellites currently used by USAP as soon as 2006. The new satellites offer increased capabilities and open the doors to new science and possibilities for observing and learning about the atmosphere, ocean, cryosphere, lithosphere, and biosphere system. However, there is a need for lead-time to prepare to acquire and train for the applications of the new streams of data.  The new satellite systems require X-band receiving equipment. One option is to utilize the existing McMurdo Ground Station (MGS) X-band receiving system. The MGS is an Earth reception station at McMurdo Station, Antarctica installed in 1993 with the goal of collecting data from Synthetic Aperture Radar (SAR) sensor equipped satellites.  Funded mutually by the National Science Foundation (NSF) and the National Aeronautics and Space Administration (NASA), this reception system has been pivotal in the collection of remotely sensed satellite data that would not be otherwise available as well as being utilized in the support of satellite and spacecraft commanding.  The goals and uses of the MGS are at a crossroad, however. Other reception systems should be considered as well. The focus of this document is to report the Antarctic science and operations community recommendations regarding the capabilities of the next generation satellite fleet along with applications and reception possibilities with a focus on the MGS, especially as it relates to USAP research and operation activities. Recommendations are given with regards to critically related communications issues as well.

# Introduction and Background

## The McMurdo Ground Station (MGS)

The MGS is a 10-meter S and X Band antenna located at McMurdo Station, Antarctica (See Figure 2). It is the result of the cooperation of two government agencies, the National Science Foundation (NSF) and National Aeronautical and Space Administration (NASA). The original purpose of the antenna was to collect   the radar mapping of the entire Antarctic continent by satellites, along with two other similar ground stations elsewhere on the continent. This station is designed to collect SAR image data from a number of international satellites over the next several years. It has been actively engaged in this activity for several months. It became active in January 1995 and was operational a year later. As early as March 1996 it was collecting 105 Mbps telemetry (X-Band) on about 25 passes each day, from ERS-1 & ERS-2 (European Earth Resource Satellites). For many of the years since, it has been supporting the Canadian SAR mapping of Antarctica with the RADARSAT satellite. It is collecting 85 Mbps and 105 Mbps telemetry routinely and using a Track and Data Relay Satellite (TDRS) link to forward that data back to Continental United States (CONUS). MGS has also supported the Southern Hemisphere science campaign of NASA's FAST mission, which is an S-Band mission.

Figure 1 A photograph of the McMurdo Ground Station 10-meter antenna (without the radome) taken in December of 1993 (Courtesy of M. Comberiate).

In August 1997, this McMurdo Ground Station (MGS) was configured quickly to command at S-Band as well. The capability had been built in but not used for any flight missions until the Lewis Satellite started tumbling. Because MGS could see virtually every pass, it was a real asset in the rescue attempt. Both store and forward commanding and real-time commanding were used. All commanding was initially tested on the active FAST satellite, using the 128Kbps full duplex channel on NSF's T1 Commercial service (available 24 hours/day). MGS inherently has the capability to support polar-orbiting satellites of all kinds, such as those that are in NASA's Mission to Planet Earth. These satellites generate in excess of 100Mbps telemetry rates due to the high-resolution images of the Earth processes that they capture. This new antenna can automatically track and collect data from multiple satellites. (With so many satellite passes that are visible from McMurdo, the MGS has to schedule which ones it will acquire).

Only a few other ground stations have the capability of MGS to unload the enormous volume of data that a polar ground station can collect. This is because of NASA's McMurdo TDRSS Relay System (MTRS). Since January 1996, a TDRS link on Black Island has been returning extremely high rate data to CONUS. It can return 300 Mbps with 10 dB margins, and has routinely been used to unload the highest volume MGS data. The only limitations to date have been on available ground equipment in CONUS to handle this high-speed data, since it is not the current norm. MGS has been used often for launch supports, where (like its 2-meter predecessor, NAILS) the telemetry it collects is returned to the control center in CONUS during or immediately following the pass. In figure 2, the photos show the large radome that is situated on one of the highest hills around McMurdo (Arrival Heights). From this vantage point it has a fantastic view in all directions and looking south it can see satellites on the other side of the South Pole.

Figure 2 A three-panel photograph of the complete McMurdo Ground Station radome that depicts its location atop Arrival Heights at McMurdo Station, Antarctica (Courtesy of M. Comberiate).

#### Technical Specifications for the McMurdo Ground Station

#### (Courtesy of M. Comberiate)

| Coordinates | 77 50' 20.87" S x 193 19' 58.50" W |
| --- | --- |
| Altitude | 150.00 meters |
| Mount: | Az-El with Tilt, no keyhole limitations |
| Diameter: | 10 meter dish |
| Antenna Gain | 45.0 (S-Band); 56.0 (X-Band) |
| Beam width: | 0.91 deg (S-Band); 0.26 deg (X-Band) |
| G/T @ Zenith: | 21.5 dB/K (S-Band); 31.8 dB/K (X-Band) |
| Transmit Frequencies: | 2000 to 2100 MHZ (S-Band) |
| Uplink Power Amplifier: | 200 Watts |
| Receive Frequencies | 2200 to 2400 MHz (S-Band) & 8025 to 8400 MHz (X-Band) |
| Freq Resolution | 50KHz |
| Rcvr Dynamic Range | 130 dB |
| LO Ref Freq Stability | + 1000 |
| Threshold | - 150 dBm @ 10KHz |
| Loop BWs | 30Hz, 100Hz, 300Hz, 1kHz, 3kHz |
| Sweep Range | + 250 kHz |
| Pointing | Autotrack, Program, or Slave |
| Slew Range | 0 to 10 deg/sec in EL; 0 to 17 deg/sec in AZ |
| Polarization | RHC/LHC |
| Telemetry Options | BPSK, PM, FM, AM (S-Band); QPSK (X-Band) |
| Symbol Rate Range | 10 to 4Msps (S); 85 & 105 Msps (X) |
| Subcarrier/Symbol rate limit | > 1.5 |
| Data Format | Source Packet |
| Modulation Options | NRZ-X, BiO-X, SAR Data (X-Band) |
| Mod Index range | 0.2 to 2.8 radians, peak |
| Subcarrier Frequency Range | 0.5 to 4 MHz (S); 60 & 105 MHz (X) |
| Subcarrier Waveform | Sine; Stability + 10E-5 |
| Data Transmission: | Transfer Frame, with Reed-Solomon Channel Coding |
| Frequency Standard & Stability | Crystal Oscillator Datum 9390 10E-11 stability @1sec; 8x10E-9 @ 1 hr; 10E-10 @ 24 hr; 10E-11@mo |

## McMurdo Station Meteorological Satellite Direct Readout History

Since the early 1980s, McMurdo Station has had the ability to receive satellite imagery directly from the NOAA, and later DMSP satellites.  Initial capabilities were analogue hard copy reception, and later moved to a digital/computer display and reception system for HRPT NOAA and RTD DMSP data (Wiesnet et al. 1980, Office of Polar Programs 1988; Van Woert et al. 1992; Lazzara et al. 2003).  The primary use of this system was for weather forecasting (Foster, 1982) and secondarily for research activities (Wiesnet et al. 1980).  Data from this system was archived and made available to the community at large primarily by the Arctic and Antarctic Research Center (AARC) and as a backup by the Antarctic Meteorological Research Center (AMRC) (Lazzara et al. 2003).

Today, these reception capabilities are installed atop Building 165, with two Sea Space Corporation antenna systems – one devoted to NOAA satellite direct readout and one devoted to DMSP satellite direct readout (See Figure 3).  SeaWiFS direct readout has a partial share of reception time during the operational field season.

Figure 3 Photo of McMurdo Operations/McMurdo Weather building 165 showing the two Sea Space NOAA and DMSP direct readout reception systems on the left hand side of the building. The system on the right is no longer installed. (Photo courtesy, NSF-OPP)

# Communications

## Present Status

The success of the McMurdo Ground Station and direct readout reception systems at McMurdo Station requires communications, specifically sufficient Internet communications bandwidth on and off station.  Currently and for the last 15 years, McMurdo Station Internet communications is a T1 satellite link via geostationary satellite (Office of Polar Programs, Pers. Comms.). Roughly half of the T1 is used for 7 telephone lines. The remaining bandwidth has been increasingly used over the years by science projects, e-mail communications, World Wide Web usage, operational usage, etc. The last several field seasons, the bandwidth has become nearly saturated in both inbound and outbound directions. (Noted at the USAP Antarctic Operations and Engineering Conference in 2003).

At the workshop, the community quickly denoted the critical importance of communications to the success of any ground station operation for both the benefit of operations and science – on and off station. It is felt that the value of any ground station or direct readout system is tremendously increased with reliable and adequate communications.

## Future Requirements

With the goal of improving inter-station Internet communications, the community recommends a set of short-term, mid-term and long-term solutions that will give tremendous value to the McMurdo Ground Station and to McMurdo Station hosting the reception of a direct broadcast data.

### Short Term

In the near term, the community strongly recommends that the National Science Foundation consider two options. The first is to acquire a second T-1 Internet connection for a period of roughly three years. This may be an expensive option, from the point of view of direct costs to NSF, as costs could run $700,000 for 3 years. Another near term option is to make arrangements with NASA for having the McMurdo TDRSS Relay System (MTRS) behave just like the South Pole TDRSS Relay (SPTR) and treat McMurdo Station as an “Instrument on a satellite.” This could give McMurdo Station dedicated or near dedicated T-3 bandwidth.  Costs to set this up could range in the more affordable $100,000 for ground station changes.  Regardless of the path taken, the community recommends that NSF set up a study of the feasibility of a dual fiber optic line between New Zealand and McMurdo Station/Scott Base. At a cost of roughly $200,000 dollars or less, such a study could lead toward giving Antarctica significant connectivity on the order of 22 Gigabyte per second.  The model for this might be the connectivity that Norway has setup between the Norway mainland and Svalbard.

### Mid Term

In the mid-term, one serious possibility is to have the USAP piggyback onto the Integrated Program Office’s (IPO) NPOESS data relay plans set for 2008.  This data relay is designed to capture and retransmit back to CONUS NPOESS satellite data.  This data relay system is specified to have a T-3 line out from McMurdo Station, but a T-1 in. It in essence requires a joint SATCOM purchase coordinated between NSF and IPO with usage allotted as required by IPO and the remainder used by NSF/USAP.  It is hoped during the midterm, the feasibility study of fiber optic lines would be completed and made available to the USAP/NSF community for open discussion.

### Long Term

In the long term, two or three options exist including the installation of fiber optic line, specifically 2 lines for redundancy, between McMurdo Station/Scott Base and New Zealand.  Other options that exist include satellite communications from either Polar sitter satellites using solar sail technology (See Figure 4) (McInnes and Mulligan, 2003) or Molniya orbiting satellites (See Figure 5 a and b) (Lazzara et al. 2003). Polar sitter satellites offer the first real possibility for the polar regions of the world to have continuous satellite coverage. Molniya satellites offer pseudo-geostationary like coverage for a roughly 8-hour period (4-hours before and after apogee). Although both of these options may be expensive, they offer the possibility of megabytes to gigabytes per second or more bandwidth service to and from McMurdo Station and many other locations in Antarctica, such as South Pole with perhaps fairly good reliability.  This report strongly encourages the polar sitting satellite concept between the two satellite concepts, given the possibility of such missions being multi-agency, and thus reducing the costs and risks for the USAP.  It is clear that if it is at all possible to have fiber optic line installed between McMurdo Station and New Zealand that such a prospect offers perhaps the best bandwidth possibilities today.

Figure 4 NOAA's vision for the future satellite series, including two polar sitting satellites - one for the Arctic and one for the Antarctic. (Courtesy Pat Mulligan/NOAA)

ab

Figure 5 a) the orbit of a Molynia satellite, with the best view over the Arctic/Northern Hemisphere region: Similar orbit could be setup for the Antarctic.  b) the ground track for the Molynia satellite.  Note on both figures, there is a dot placed 4 hours before and 4 hours after apogee. [From Kidder and Vonder Haar (1991).]

# Science and Operational Requirements

## Scope and Effects

Currently, the McMurdo Ground Station, and other direct readout systems at McMurdo are capable of retrieving local coverage, especially with satellites that have limited on-board storage, and work well the reception of direct broadcast data (RADARSAT in the case of MGS and NOAA, DMSP, and SeaWiFS in the case of the meteorology direct readout systems at Mac Weather, etc.)  The future use of these systems impacts science and operations. One concern with these systems is the lack of historical reliability of the MGS system. There is a need to prove the MGS can perform at minimal costs or alternatively price out the costs of a second, stand along direct readout system that can be used for the reception of data in support of science and operations. In this same vein, there is also a need to assess the cost differences and benefit differences between a stand-alone direct readout system with X-band reception capabilities as compared to the cost system improvements to the existing operational L-band systems with limited reception abilities and leaving the MGS system aside.  Will the next generation satellites broadcast of information via L-band transmission for targeted environmental data records (EDR) are enough for science and operational applications for the USAP? (See Appendix for more on X- vs. L-band EDR as defined by IPO).

It is becoming more and more clear, that the applications of satellite data observations from X-band broadcast platforms such as Aqua and Terra satellite are having impacts in the polar and middle latitude regions such as the use of polar orbiting satellite observations assimilated into a numerical weather prediction model impacting and improving the forecast for a snow event in the middle latitudes (Key, Pers. Comms. 2003). Non-traditional data sets such as direct broad data could provide the only means of economical data collection for Antarctica and the Southern Ocean.  Further more, there are still more areas of research needed to put such data to use.  For example, many algorithms and applications of satellite data applications from Mission to Planet Earth satellites (Terra and Aqua), are global in focus.  There are needs to modify these algorithms and methods for use in the Antarctic and South Ocean region (Menzel, Pers. Comms., 2003).

## Multi-discipline Benefits

It is clear that the future will bring more demand and growth for the usage of data both on station and off station.  Here is a sample list of the cross-discipline range of possibilities:

- Real-time satellite data available for assimilation into the Antarctic Mesoscale Prediction System (AMPS) and Polar MM5 modeling systems at National Center for Atmospheric Research and the Ohio State University.

- Real-time use in science support of future McMurdo area Long Term Ecological Research (LTER) project with sea ice state information

- Real-time use for weather forecasting for USAP Flight, station and ship operations.

- Ocean color plankton/marine science studies

- Geology land resource applications

- Glaciological feature studies/iceberg studies and tracking/monitoring

- Sea ice formation, detection, and tracking

- Cloud/fog recognition products – Fog detection

- Cloud droplet products - Aircraft Icing, and potential snowfall

- Wind, Temperature, and Humidity profiling – Improved analysis for Forecaster and Numerical data input

- Daily Surface Reflectance - Global change

- Cryosphere identification by class – Blowing Snow forecasting

- Land and Ocean Surface temperature – McMurdo sound potential icing conditions

With readily available data, this list will likely grow.

## Impacts

With the combined improvements in communications and reception of direct broadcast from the next generation satellite series, impacts will ripple through both the science and operational communities. A sample of possible improvements were noted at the workshop including:

- Global model improvements using information from the Antarctic in real-time.

- Timely availability of products to global modeling centers, weather forecasters on and off continent, real-time science data available to researchers, and polar remote sensing data available to the educational community via existing NSF funded projects (e.g. Unidata project).

- Availability of derived products on the World Meteorological Organization’s (WMO) Global Telecommunications System (GTS).

## Implementation

One of the key topics discussed at the meeting was the utility of the data.  With the ability to receive the data, and with good communications, issues with regards to data processing location, real-time use of the data in both the operational and research arenas, and data format and easy interactive processing become critical issues.

The state of communications clearly dictates the possibilities of data processing on station, off station or a combination of the two.  Without significantly improved communications, it is impossible to import or export high volume data, even data in a raw, data stripped, and/or compressed format.  Next generation satellites, especially those transmitting direct broadcast data in the X-band range, have gigabytes of data available daily.  The ability to send this data over smaller communication methods is impossible.  With improve bandwidth, it maybe possible to have data captured at McMurdo Station and be sent off site for additional data processing, and/or have data received and processed at other locations be imported to McMurdo Station. With applications that require timely, real-time data, such as weather forecasting, numerical weather prediction, etc. some combination of these options will prove best. For example, weather forecast operations on station may require data to be received and processed on station to provide the data as soon as possible to the forecaster.  However, for numerical weather prediction, data received on station may not need to be completely processed on site, but partially processed, with the remaining processing done at the numerical weather prediction center or institution.  In the NPOESS era, data may not need to be received on location at all, as the NPOESS/IPO SafetyNet will provide data to numerical weather prediction centers within ~28 minutes of reception.

One key need for everyone, and especially the research community, is the format and ease of working with the data via interactive processing systems. There is unfortunately no one size fits all for both of these topics.  However, it is strongly recommended that regardless of choice of interactive display and processing system that it is able to convert between various formats of choice of the satellite operators.  Likewise it is the advice of this report that any selected formats are well documented, non-propriety, and if at all possible, a self-describing format.

### Short Term

The community at the workshop has identified an immediate short-term demonstration of the capabilities of the McMurdo Ground Station. The goal is to generate cloud drift wind datasets, two times a day, from a set (2 triplets or three successive passes of Aqua/Terra data two times a day) of MODIS imagery acquired by the McMurdo Ground Station (MGS).  We learned at the meeting that the MGS does have a one-way-out electronic networking capability.  Given that critical piece of information, it is possible to have the MGS folks acquire these passes and send them to the AMRC office [in Crary Lab] for further processing.  At the AMRC office [in Crary lab], this raw pass data would be received by a computer system that Jeff Key's group at the University of Wisconsin would set up to process the raw passes into science level data (Level 1b HDF-EOS), and in turn make the cloud drift winds.  The cloud drift wind sets, being so much smaller than the raw data (on the order of kilobytes large), could then be sent back to the US for a variety of users, including, the NCAR/MMM AMPS group, the Ohio State/BPRC Polar MM5 group, NASA Global Modeling and Assimilation Office (GMAO) group, and used here at Wisconsin as well.  Meanwhile, the Operational Weather Forecasters at McMurdo Weather would also benefit by being able to view the raw imagery, the cloud drift wind sets and any other products we can generate on station (since there is not a bandwidth limit for moving data around the station, for the most part).

### Mid Term

In the mid term, the community strongly recommends the installation of a stand along direct readout system that is not a part of the McMurdo Ground Station.  This system, perhaps as small as 3 or 4 meters in diameter, would be have X-band, S-band and L-band capabilities.  This system would be an automated system, devoted to receiving data from currently active satellites such as Aqua, Terra, ENVISAT, etc. and would be in a position to receive direct broadcasts from the NPP, NPOESS, and other satellites to be launched in the future.

The community also discussed having this kind of support and capability at both South Pole and Palmer Stations for science.

In the mid-term, the community notes that the applications and users of datasets from the short-term activities will be broadened.    This is natural, especially with the enactment of recommendations made with regards to communications.

### Long Term

In the long-term, the United States Antarctic Program, as well as other national Antarctic programs will be entering the NPOESS era (See Figures 4 and 5).  This era ushers in new investments in science, including the widely discussed International Polar Year [(PY) (NRC, 2004), Ross Island Meteorology Experiment (RIME) (Parish and Bromwich, 2002), future long term ecological research projects, West Antarctic Ice Sheet Ice Core (WAIS Core) projects, etc.

Figure 6 During the next several years, there is an evolution of satellites towards the NPOESS era.

Figure 7 The transition from the current satellite system to the new generation satellite system depicts the timelines and "bridge" missions into the future.

The USAP is currently at a cross roads with regards to its long-term satellite reception future at McMurdo Station: Will it be able to receive and utilize high-resolution data (HRD) or low-resolution data (LRD) rate from NPOESS?  Clearly, LRD data will be an improvement over the current HRPT and RTD systems with NOAA and DMSP, and there is no operational requirement for the HRD data (Cayette, 2002; Cayette, 2003). However, as of the publishing of this report, the content of the LRD data stream is not yet completely defined, although the products that can be produced from that yet-to-be-defined data stream are.  In addition, it is not clear from the point of view of research activities if LRD data from NPOESS will be sufficient: Advances made using HRD data will not be able to be implemented at McMurdo Station, without a means of getting that data.

# Limiting Factors

It is clear from the discussions and issues raised at the workshop and in this report there are some clear limiting factors that impede the viability of the McMurdo Ground Station, and the reception and use of direct broadcast satellite data.  Discussion on communications and infrastructure are discussed below.

## Communications

Aside from the obvious limits that no improvements in Internet communications to and from McMurdo Station presents, there are some specific limitations that are important to denote with regards to the communication solutions presented in this report.

### Closed Network

The MGS is not readily available for use on station because it is on a closed network, which poses a clear limitation.  The inability to utilize the data received by the system on station limits the use of the ground station for real-time data.  With no easy paths for the data, it only serves best for research projects that do not need the data in real-time, especially with spacecraft that do not have a store and forward capability such as RADARSAT.

### McMurdo TDRSS Relay System (MTRS)

With the possible option to have the MTRS used as a means for Internet communications for McMurdo Station, targeted for science and operational use much like the South Pole TDRSS Relay System, there will be some issues that may limit the viability of the system. Visibility of TDRSS satellite series may pose a problem, as currently there is only 1 TDRSS system available to McMurdo for a limited time.  Two TDRSS satellites would need to be available to give 24 hours, 7 days per week coverage for a constant connection. Scheduling TDRSS time may be a problem as well. Unlike the SPTR system, NASA may not be able to offer a dedicated TDRSS system. Sharing a TDRSS system with Space Shuttle or other NASA missions may not give McMurdo the timely connectivity required.  Finally, the MTRS is at present setup to be on a closed network.  This would have to change to be more like the SPRT system to give open access to a variety of sites off station.

## Infrastructure

In reviewing the state of the MGS, and direct readout systems on station there are some clear infrastructure issues that need to be addressed for either system to be viable in the future.

Discussions at the workshop clearly indicated that the MGS’s reliability has been an issue over the years.  The MGS and associated facilities at Wallops Flight Facility (WFF) in Virginia may be in need of infrastructure upgrades. Apparently a set of upgrades is (or at least were) needed.  For example, there was an inability to efficiently accommodate rescheduling of the downlinks to MGS during the 2000 MAMM mission.  This was partly a WFF issue and partly a MGS local issue.  The viability of the MGS is at stake; otherwise the MGS is irrelevant unless the station is reliable.

Concerns have been raised regarding local processing power and data storage at McMurdo Station.  These problems are becoming more easily solved, as computing and data storage becomes less expensive. The bottom line is that resources such as these will be needed to utilize observations from next generation satellite system.

# Conclusions and Recommendations

This report, based on the discussions with the science and operational community at both the workshop and afterwards, has the following specific recommendations:

- Recommend that the United States Antarctic Program actively pursue increased and improved Internet communications both to and from McMurdo Station, Antarctica

- Recommend the installation of a stand-alone direct readout reception station for science and operational use by the United States Antarctic Program and its partners.

- Recommend the processing and use of direct broadcast data be required both on site at McMurdo Station as well as off site.

- Recommend that if the MGS is to remain a viable ground station that sufficient monies for MGS are required to adequately manage and maintain MGS so as to insure a year round reliability consistent with other satellite ground stations.

# Acknowledgements

The editors wish to thank Lynn Everett, David Bromwich, and Andy Monaghan at the Byrd Polar Research Center at the Ohio State University, and Marlene McCaffery at the Space Science and Engineering Center, University of Wisconsin-Madison.  Their help made this workshop come to life. We wish to acknowledge all of the workshop participants who helped to make the workshop, and in turn, the report a success.  We wish to thank the Office of Polar Programs, National Science Foundation, grant number OPP-0412586 without whose funding this workshop would have not been possible.

# References

Cayette, A., 2003: Recommended Timeline for the Receipt of X-Band Operational Weather Satellite Data Revision 1.0, Unpublished.

Cayette, A., 2002: Meteorology Satellite Requirements for Operations Conducted by the United States Antarctic Program. Unpublished.

Lazzara, M.A., L.M. Keller, C.R. Stearns, J.E. Thom, and G.A. Wiedner, 2003: Antarctic Satellite Meteorology: Applications for Weather Forecasting. Monthly Weather Review, 131, 371-383.

Lazzara, M. A.  Meteorological satellite status report for SPAWAR Systems Center Charleston, Aviation Technical Services and Engineering Division (Code 36), N65236-02-P-1646.  Madison, WI, University of Wisconsin-Madison, Space Science and Engineering Center, Antarctic Meteorological Research Center, 2002.  UW SSEC Publication No.02.06.L1a.

McInnes, C.R., and P. Mulligan, 2003: Final Report: Telecommunications and Earth Observations Applications for Polar Stationary Solar Sails. Report to the National Oceanic and Atmospheric Administration (NOAA) from the Department of Aerospace Engineering, University of Glasgow. 24 January 2003.

Nelson, C.S., and J.D. Cunningham, 2002: The National Polar-Orbiting Operational Environmental Satellite System Future U.S. Environmental Observing System. 6th Symp. on Integrated Observing Systems, Orlando, FL (USA), American Meteorological Society, 13-17 Jan 2002

National Research Council (NRC). 2004. A Vision for the International Polar Year 2007-2008. Washington, D.C.: National Academy Press.

Office of Polar Programs, 1988: McMurdo Station gets satellite-image processing system. Antarct. J. U.S., 23, 8-9.

Parish, T.R., and D.H. Bromwich (eds.), 2002: Ross Island Meteorology Experiment (RIME) Detailed Science Plan. BPRC Miscellaneous Series M-424, Byrd Polar Research Center, The Ohio State University, Columbus, Ohio.

Wiesnet, D. R., C. P. Berg, and G. C. Rosenberger, 1980: High resolution picture transmission satellite receiver at McMurdo station aids Antarctic mosaic project. Antarct. J. U.S., 15, 190–193.

Van Woert, M. L., R. H. Whritner, D. E. Waliser, D. H. Bromwich, and J. C. Comiso, 1992: Arc: A source of multi-sensor satellite data for polar science. Eos, Trans. Amer. Geophys. Union, 73, 65, 75–76.

# Appendices

## Web sites

http://www.nsf.gov/

http://www.nsf.gov/od/opp/start.htm

http://amrc.ssec.wisc.edu/

http://amrc.ssec.wisc.edu/MGS

http://arcane.ucsd.edu

http://www.npoess.noaa.gov

http://npoesslib.ipo.noaa.gov

http://www.esa.int/export/esaSA/ESAOC976K3D_earth_0.html

http://www.esa.int/export/esaCP/SEMXVFXLDMD_Protecting_0.html

http://www.isc.nipr.ac.jp/office/SATELLITE/satellite.html

http://www.us-ipy.org/index.html

http://seawifs.gsfc.nasa.gov/SEAWIFS.html

http://oceancolor.gsfc.nasa.gov/

## Acronyms

AARC		Arctic and Antarctic Research Center

AMPS		Antarctic Mesoscale Prediction System

AMRC		Antarctic Meteorological Research Center

AVHRR	Advanced Very High Resolution Radiometer

CONUS	Continental United States

DMSP		Defense Meteorological Satellite Program

EDR		Environmental Data Records

ENVISAT

EOS		Earth Observing System

FAST

GMAO	Global Modeling and Assimilation Office

GTS		Global Telecommunications System

HRD		High Resolution Data

HDF		Hierarchal Data Format

HRPT		High Resolution Picture Transmission

IPO		Integrated Program Office

IPY 		International Polar Year

LRD		Low Resolution Data

MAMM	Modified Antarctic Mapping Mission

Mbps		Megabits per second

MGS		McMurdo Ground Station

MM5		Mesoscale Model version 5 (Penn State/NCAR)

MMM		Mesoscale, Microscale Meteorology

MODIS	Moderate resolution Imaging Spectroradiometer

MTRS		McMurdo TDRSS Relay System

NSF		National Science Foundation

NAILS

NASA		National Aeronautics and Space Administration

NCAR		National Center for Atmospheric Research

NOAA		National Oceanographic and Atmospheric Administration

NPOESS	National Polar Orbiting Environmental Satellite System

NPP		NPOES Preparatory Platform

OPP		Office of Polar Programs

RADARSAT

RIME		Ross Island Meteorology Experiment

RTD		Real Time Data

SAR		Synthetic Aperture Radar

SATCOM	Satellite Communications

SeaWiFS	Sea Wide Field Sensor…..

SPTR		South Pole TDRSS Relay

T1

T3

TDRSS	Tracking Data and Relay Satellite System

USAP		United States Antarctic Program

WAIS		West Antarctic Ice Sheet

WFF		Wallops Flight Facility (NASA)

WMO		World Meteorological Organization

## NPOESS Sensors and Capabilities

## Workshop Attendees

Don Atwood

Alaska Satellite Facility

Geophysical Institute

903 Koyukuk Dr.

P.O Box 757320

Fairbanks AK 99775-7380

datwood@asf.alaska.edu

Phone: 907-474-7380

David Bromwich

Byrd Polar Research Center

108 Scott Hall, 1090 Carmack

Columbus OH 43210

bromwich.1@osu.edu

Phone:614-292-6692

Fax: 614-292-4697

John Cassano

CIRES/PAOS

University of Colorado at Boulder

216 UCB

Boulder CO 80309-0216

cassano@cires.colorado.edu

Phone: 303-492-2221

Fax: 303-492-2221

Art Cayette

Space Naval Warfare System Center

1 Innovation Drive

North Charleston SC 29419-90022

Arthur.cayette@navy.mil

Phone: 843-218-4945

Steve Colwell

British Antartic Survey

High Cross, Madingley Road

Cambridge UK CB3 0ET

src@bas.ac.uk

Phone: 44 1223 221 447

Fax: 44 1223 221 279

Mike Comberiate

NASA Goddard Space Flight Center

Greenbelt  MD 20771

mcomberi@pop400.gsfc.nasa.gov

Phone: 301-286-9828

Josefino Comiso

Laboratory for Hydrosperic Processes Code 971

NASA Goddard Space Flight Center

Greenbelt MD20771

Josefino.C.Comiso@nasa.gov

Phone: 310-614-5708

Fax: 310-614-5644

Curtis Emerson

NASA Goddard Space Flight Center

Mission Services Program Office

Code 453

Greenbelt MD 20771

Curtis.M.Emerson@nasa.gov

Phone: 301-286-7670

Fax: 301-286-0328

Lynn Everett

Byrd Polar Research Center

108 Scott Hall, 1090 Carmack

Columbus OH 43210

everett.2@osu.edu

Phone:614-292-9909

Fax: 614-292-4697

Mark Fahnestock

CSRL/EOS

236A Morse Hall

University of New Hampshire

Durham NH 03824

mark.fahnestock@unh.edu

Phone: 603-862-5065

Andrew Fleming

Brtitsh Antartic Survey

High Cross, Madingley Road

Cambridge UK CB3 0ET

ahf@bas.ac.uk

Phone: 44 1223 221 447

Fax: 44 1223 362616

Ryan Fogt

Byrd Polar Research Center

108 Scott Hall

1090 Carmack Road

Columbus OH43210

rfogt@polarmet.mps.ohio-state.edu

Phone: 614-292-1060

Fax: 614-292-4697

James Frodge

Space Naval Warfare System Center

1 Innovation Drive

North Charleston SC 29419-90022

james.frodge@navy.mil

Phone: 843-218-4287

Toufic (Tom) Hawat

Denver University

2112 E. Wesley Ave.

Denver CO 80222

thawat@du.edu

Phone: 303-871-3547

Fax: 303-871-4405

Kathie Hill

Raytheon Polar Services

7400 South Tuscon Way

Centennial CO 80112-3938

Kathi.Hill@usap.gov

Phone: 720-568-2344

Fax: 303-792-9066

Kenneth Jezek

Byrd Polar Research Center

108 Scott Hall

1090 Carmack Road

Columbus OH 43210

jezek@frosty.mps.ohio-state.edu

Phone: 614-292-7973

Fax: 614-292-4697

Jeff Key

NOAA/NESDIS

1225 West Dayton Street

Madison WI 53706

jkey@ssec.wisc.edu

Phone: 608-263-2605

Fax: 608-262-5974

Matthew Lazzara

AMRC/SSEC

University of Wisconsin-Madison,

947 Atmospheric, Oceanic and Space Science Building

1225 West Dayton Street

Madison WI 53706

mattl@ssec.wisc.edu

Phone: 608-262-0436

Fax: 608-263-6738

Bernhard Lettau

National Science Foundation

Office of Polar Programs

4201 Wilson Boulevard

Room 755 S

Arlington VA 22230

blettau@nsf.gov

Phone: 703-292-7416

Dan Lubin

Scripps Institution of Oceanography University of California, San Diego

9500 Gilman Drive

La Jolla CA 92093-0221

dlubin@uscd.edu

Phone: 858-534-6369

Fax: 858-534-7452

Berry Lyons

Byrd Polar Research Center

108 Scott Hall

1090 Carmack Road

Columbus OH 43210

lyons.142@osu.edu

Phone: 614-688-3241

Fax: 614-292-4397

Andrew Monaghan

Byrd Polar Research Center

108 Scott Hall

1090 Carmack Road

Columbus OH 43210

monaghan.11@osu.edu

Phone: 614-247-6789

Fax: 614-292-4397

John Overton

NPOESS Integrated Program Office Suite 1450

8455 Colesville Rd

Silver Spring MD 20910

John.overton@noaa.gov

Phone: 301-713-4747

Fax: 301-427-2164

Haley Shen

Department of Civil & Environmental Engineering Clarkson University

Potsdam NY 13699-5710

hhshen@clarkson.edu

Phone: 315-268-6614/6006

Fax: 315-268-7985

Walker Smith

Virginia Institute of Marine Science College of William and Mary

Gloucester Point VA 23062

wos@vims.edu

Phone: 804-684-7709

Fax: 804-684-7399

Charles Stearns

AMRC/SSEC

University of Wisconsin-Madison

947 Atmospheric, Oceanic and Space

Science Building

1225 West Dayton Street

Madison WI 53706

Chucks@ssec.wisc.edu

Phone: 608-262-0780

Fax: 608-263-6738

Towanda Street

Science and Applied Technology

Department Head

National/Naval Ice Center

4251 Suitland Road

Washington DC 20395

tstreet@natice.noaqa.gov

Phone: 301-394-3104

Fax: 301-394-3200

Graham Tilbury

Center for Ocean Technology

University of South Flordia

St Petersburg FL 33701

gtilbury@seas.marine.usf.edu

Phone: 727-553-3989

Fax: 727-553-3967

Scott Turek

Raytheon NPOESS

16800 E CentreTech Parkway

DN, Bldg. 577  M/S 2011

Aurora  CO 80011

rsturek@raytheon.com

Phone: 720-858-5266

Fax: 303-344-6439

James Valenti

NPOESS

8455 Colesville Road

Suite 1450

Silver Spring  MD 20910

James.Valenti@noaa.gov

Phone: 301-713-4744

Fax: 301-427-2164

Bill Watson

NASA Headquarters

Code YF

Washington DC 20546

Bill.Watson@nasa.gov

Phone: 202-358-4689

Fax: 202-358-2769

Yanqui Zhu

Global Modeling Assimilation Office

NASA Goddard Space Flight Center

Greenbelt MD 20771

zhu@gmao.gsfc.nasa.gov

Phone: 301-614-5858