### Antarctic Automatic Weather Station Data

for the calendar year 2009

by

# Linda M. Keller

Matthew A. Lazzara

Jonathan E. Thom

George A. Weidner

Charles R. Stearns

Space Science and Engineering Center

University of Wisconsin

1225 W. Dayton St.

Madison, Wisconsin

October, 2010

# Antarctic Automatic Weather Station Data

# For The Calendar Year

2009

by

# Linda M. Keller

Matthew A. Lazzara

# Jonathan E. Thom

# George A. Weidner

# Charles R. Stearns

# Space Science and Engineering Center

# University of Wisconsin

# 1225 W. Dayton St.

# Madison, Wisconsin

October, 2010

# TABLE OF CONTENTS

# Page

1.  Introduction.........................................................................................................................	  1

2.  Data Transmission..............................................................................................................   	  1

3.  AWS Identification and Location......................................................................................... 	  1

4.  AWS Data Summaries........................................................................................................   	  8

4.1. Monthly Data Summaries..............................................................................................  	  8

D-10..............................................................................................................................	  9

D-47..............................................................................................................................	  9

D-85……………………………………………………………………………………………..    9

Dome C II..................................................................................................................... 	 10

Cape Denison………………………………………………………………………………….	 10

E-66…………………………………………………………………………………………….     10

Byrd……………………………………………………………………………………………..    11

Mount Siple...................................................................................................................  	 11

Theresa…………………………………………………………………………………………    11

Elizabeth....................................................................................................................... 	 12

Brianna…………………………………………………………………………………………    12

Harry……………………………………………………………………………………………	 12

Erin............................................................................................................................... 	 13

Siple Dome................................................................................................................... 	 13

Swithinbank................................................................................................................... 	 13

Kominko-Slade………………………………………………………………………………...    14

Marble Point..................................................................................................................	 14

Ferrell............................................................................................................................ 	 14

Pegasus North...............................................................................................................	 15

Minna Bluff.................................................................................................................... 	 15

Linda............................................................................................................................. 	 15

Willie Field....................................................................................................................	 16

Windless Bight..............................................................................................................	 16

Cape Bird....................................................................................................................... 	 16

Laurie II……..................................................................................................................	 17

Lorne…………………………………………………………………………………………….   17

Mulock…………………………………………………………………………………………..   17

Mt. Fleming……………………………………………………………………………………..   18

Possession Island..........................................................................................................	 18

Manuela.........................................................................................................................	 18

Marilyn...........................................................................................................................	 19

Schwerdtfeger................................................................................................................	 19

Gill.................................................................................................................................	 19

Lettau............................................................................................................................	 20

Vito………………………………………………………………………………………………   20

Emilia……………………………………………………………………………………………   20

Carolyn………………………………………………………………………………………….   21

Mary……………………………………………………………………………………………..   21

Eric………………………………………………………………………………………………   21

Margaret…………………………………………………………………………………………  22

Larsen Ice Shelf.............................................................................................................	 22

Butler Island................................................................................................................... 	 22

Fossil Bluff…..…………………………………………………………………………………..  23

Limbert.......................................................................................................................... 	 23

Bonaparte Point.............................................................................................................	 23

Sky-Blu.......................................................................................................................... 	 24

Dismal Island…………………………………………………………………………………..    24

Hugo Island…………………………………………………………………………………….    24

Henry............................................................................................................................. 	 25

Nico............................................................................................................................... 	 25

Mizuho………………………………………………………………………………………….    25

Baldrick…………………………………………………………………………………………    26

JASE2007……………………………………………………………………………………...    26

PANDA-South………………………………………………………………………………….    26

4.2. Three Hourly Data Summaries....................................................................................... 	 27

5.   AWS Calibration................................................................................................................. 	 27

5.1. Temperature................................................................................................................. 	 27

5.2. Pressure....................................................................................................................... 	 27

5.3. Wind Direction and Speed............................................................................................ 	 27

5.4. Relative Humidity......................................................................................................... 	 28

5.5. Vertical Air Temperature Difference.............................................................................. 	 28

5.6. Acoustic Depth Gauge………………………………………………………………………...  28

6.   AWS Operations Summary for 2009...................................................................................	 28

6.1. AWS Performance........................................................................................................ 	 28

6.2. AWS Antarctic Field Activities....................................................................................... 	 30

7.   Global Telecommunications System.................................................................................... 	 31

8.   Data Availability................................................................................................................... 	 31

9.   Acknowledgments................................................................................................................ 	 32

# 1.  INTRODUCTION

Automatic weather station (AWS) units are deployed to collect Antarctic surface weather observations in support of specific meteorological research projects as well as operational activities in Antarctica.  The 2009 network consisted of 55 installed AWS units providing observations on the Ross Ice Shelf, east of the Transantarctic Mountains and north of McMurdo to the Adelie Coast, along the Antarctic Peninsula, West Antarctica, East Antarctic, and climatological locations such as the South Pole.  Each unit measures air temperature, wind speed, and wind direction at the top of the unit's tower at a nominal height of three meters and air pressure at the electronics enclosure (Figure 1).  Some AWS units also measure the relative humidity at three meters, vertical air temperature difference between 0.5 and 3 meters, and snow accumulation.  Measurement heights relative to the actual surface at the site are nominal due to snow accumulation around the AWS unit.

# 2.  DATA TRANSMISSION

The transmitted AWS data are received and stored by the Data Collection System (DCS) on the NOAA series and MetOp series of polar orbiting satellites.  The data are retransmitted by the satellite for use in the High Resolution Picture Transmission (HRPT) broadcast at McMurdo and Palmer Station, Antarctica.  The data are processed into scientific units and are available for local use.  CLS America (Service ARGOS), Largo, Maryland, receives the complete DCS data set and sends it to the University of Wisconsin-Madison where it is processed and distributed to the users.

# 3.  AWS IDENTIFICATION AND LOCATION

Site location is defined by the latitude and longitude which is determined by various methods: sun shots, angles to geographical features, aircraft data, ice breaker data, the platform location system of CLS America (Service ARGOS), and the Global Positioning System.  AWS elevation is obtained by barometry and Global Positioning System (GPS) and should be correct to within +/- 5 meters.  Site names were introduced for convenience. Table 3.1 lists the site name, ARGOS identification number, latitude, longitude, elevation, start date for the site, and the World Meteorological Organization (WMO) number for the site.  Figures 2, and 3 show the locations of the AWS units in the Antarctic for 2009.

The ARGOS identification number (ID) is used to identify the data sets distributed to the users.  AWS units are sometimes moved from one location to another, and as a result, the ID at a given site may change from year to year. The site name does not change. Table 3.2 lists the site name with the ARGOS ID, the site start date, and the ID start and stop dates.

Figure 1.  Layout of the AWS unit used in the Antarctic.  The installed AWS unit has a 3-meter tower with a horizontal boom supporting the antenna, aerovane for measuring wind speed and direction, air temperature resistance thermometer, upper thermopile for measuring vertical air temperature difference, and the relative humidity sensor.  The electronics enclosure is mounted at the midpoint of the tower.  The gel cell batteries are placed at the tower base.  The solar panel, located near the tower top, faces north. The Acoustic Depth Gauge (ADG) is installed on some of the AWS units to measure snow accumulation.

### Table 3.1

AWS site name, geographic location and elevation, site start date, and WMO number for 2009.

| Site Name | ARGOS ID | Lat. (deg ) | Long. (deg) | Elev. (m) | Site Start Date | WMO No. |
| --- | --- | --- | --- | --- | --- | --- |
|  |  |  | Adelie Land |  |  |  |
| D-10 | 30374 | 66.71oS | 139.83oE | 243 | 08 Jan 80 | 89832 |
| D-47 | 8947 | 67.397oS | 138.726oE | 1560 | 24 Jan 83 | 89834 |
| D-85 | 8986 | 70.426oS | 134.146oE | 2682 | 10 Dec 07 |  |
| Dome C II | 8989 | 75.121oS | 123.374oE | 3250 | 12 Dec 95 | 89828 |
| Cape Denison | 8988 | 67.009oS | 142.664oE | 31 | 20 Jan 90 |  |
| E-66 | 8912 | 68.912oS | 134.655oE | 2485 | 12 Dec 07 |  |
|  |  |  | West Antarctica |  |  |  |
| Byrd Station | 8903 | 80.007oS | 119.404oW | 1530 | 05 Feb 80 | 89324 |
| Mount Siple | 8981 | 73.198oS | 127.052oW | 230 | 20 Feb 92 | 89327 |
| Theresa | 21358 | 84.599oS | 115.811oW | 1463 | 29 Nov 94 | 89314 |
| Elizabeth | 21361 | 82.607oS | 137.078oW | 519 | 30 Nov 94 | 89332 |
| Brianna | 8931 | 83.889oS | 134.154oW | 525 | 30 Nov 94 |  |
| Harry | 8900 | 83.003S | 121.393W | 945 | 29 Nov 94 |  |
| Erin | 21363 | 84.904oS | 128.828oW | 990 | 29 Nov 94 |  |
| Siple Dome | 8938 | 81.656oS | 148.773oW | 668 | 21 Jan 97 | 89345 |
| Swithinbank | 8927 | 81.201oS | 126.177oW | 959 | 18 Jan 97 |  |
| Kominko-Slade | #21364 | 79.466oS | 112.106oW | 1801 | 13 Jan 06 |  |
|  |  |  | Ross Island Region |  |  |  |
| Marble Point | 8906 | 77.439oS | 163.754oE | 108 | 05 Feb 80 | 89866 |
| Ferrell | 8929 | 77.846oS | 170.819oE | 45 | 10 Dec 80 | 89872 |
| Pegasus North | 21357 | 77.952oS | 166.500oE | 8 | 23 Jan 90 | 89667 |
|  | #8923 |  |  |  |  |  |
|  | #8937 |  |  |  |  |  |
| Pegasus South | 8937 | 77.99oS | 166.560oE | 5 | 14 Jan 91 |  |
| Minna Bluff | 8939 | 78.555oS | 166.691oE | 895 | 22 Jan 91 | 89768 |
| Linda | 21362 | 78.426oS | 168.318oE | 42 | 21 Jan 91 | 89769 |
| Willie Field | 21364 | 77.867oS | 166.957oE | 13 | 25 Jan 92 |  |
|  | #30477 |  |  |  |  |  |
| Windless Bight | 8982 | 77.723oS | 167.692oE | 40 | 09 Dec 98 |  |
| Cape Bird | 8901 | 77.217oS | 166.439oE | 38 | 28 Jan 99 |  |
| Laurie II | 21360 | 77.517oS | 170.801oE | 37 | 01 Feb 00 |  |
| Lorne | 21356 | 78.239oS | 170.006oE | 45 | 12 Jan 07 |  |
| Mulock | 8907 | 78.917oS | 159.000oE | 1000 | 24 Oct 06 |  |
| Mt. Fleming | 30393 | 77.533oS | 160.271oE | 1950 | 01 Nov 06 |  |
|  |  |  | Ocean Islands |  |  |  |
| Possession Is. | 8984 | 71.891oS | 171.210oE | 30 | 29 Dec 92 | 89879 |
| Manuela | 8905 | 74.946oS | 163.687oE | 78 | 06 Feb 84 | 89864 |
|  |  |  | Ross Ice Shelf |  |  |  |
| Marilyn | 8934 | 79.926oS | 165.494oE | 63 | 16 Jan 84 | 89869 |
| Schwerdtfeger | 8913 | 79.867oS | 170.142oE | 54 | 24 Jan 85 | 89868 |
| Gill | 8911 | 79.922oS | 178.586oW | 54 | 24 Jan 85 | 89376 |
| Lettau | 8928 | 82.481oS | 174.570oW | 39 | 29 Jan 86 | 89377 |
| Elaine | #21357 | 83.097oS | 174.291oE | 62 | 28 Jan 86 | 89873 |
| Vito | 8695 | 78.466oS | 177.782oE | 50 | 03 Feb 04 |  |
| Emilia | 8980 | 78.473oS | 173.146oE | 51 | 31 Jan 04 |  |
| Carolyn | 8722 | 79.939oS | 175.884oE | 52 | 02 Feb 05 |  |
| Mary | 8983 | 79.304oS | 162.985oE | 58 | 31 Jan 05 |  |
| Eric | 8697 | 81.504oS | 163.939oE | 45 | 29 Jan 05 |  |
| Margaret | 8910 | 80.000oS | 165.000oW | 67 | 12 Nov 08 |  |

| Site Name | ARGOS ID | Lat. (deg) | Long. (deg) | Elev. (m) | Site Start Date | WMO No. |
| --- | --- | --- | --- | --- | --- | --- |
|  |  |  | Antarctic Peninsula |  |  |  |
| Larsen Ice | 8926 | 67.01oS | 61.31oW | 35 | 07 Feb 83 | 89262 |
| Butler Island | 8902 | 72.12oS | 60.10oW | 115 | 01 Mar 86 | 89266 |
| Fossil Bluff | 8920 | 71.19oS | 68.17oW | 66 | 10 Jan 05 |  |
| Limbert | 8925 | 75.52oS | 59.09oW | 59 | 30 Nov 95 | 89257 |
| Bonaparte Pt. | 8921 | 64.778oS | 64.067oW | 8 | 05 Jan 92 | 89269 |
| Sky-Blu | 8917 | 74.792oS | 71.488oW | 1556 | 07 Feb 99 | 89272 |
| Dismal Island | 8932 | 68.087oS | 68.825oW | 10 | 27 May 01 |  |
| Hugo Island | 8935 | 64.935oS | 65.303oW | 25 | 10 Dec 94 |  |
|  |  |  | High Polar Plateau |  |  |  |
| Henry | 8985 | 89.011oS | 1.025oW | 2755 | 26 Jan 93 | 89108 |
| Nico | 8924 | 89.000oS | 89.669oE | 2935 | 26 Jan 93 | 89799 |
| Mizuho | 21359 | 70.70oS | 44.29oE | 2260 | 07 Oct 00 |  |
| Baldrick | 9116 | 82.774oS | 13.054oW | 1968 | 01 Jan 08 |  |
| JASE2007 | 30305 | 75.888oS | 25.834oE | 3661 | 27 Sep 07 |  |
| PANDA-South | 30416 | 82.325oS | 75.989oE | 4027 | 14 Jan 08 |  |

* New sites started during 2009

# New ARGOS ID for 2009 at the site

Figure 2.  Antarctic automatic weather station locations during 2009 identified by the site name. Area around Ross Island is shown in Figure 3.

Figure 3.  Location of Antarctic automatic weather stations in the vicinity of Ross Island, Antarctica during 2009.

# Table 3.2

2009 Antarctic AWS site name, ARGOS identification number (ID), site start date, ID start date, and ID stop date if occurring in 2009.

| Site | ARGOS ID | Site Start Date | ID Start Date | ID Stop Date |
| --- | --- | --- | --- | --- |
| D-10 | 30374 | 08 Jan 80 | 01 Feb 08 |  |
| D-47 | 8947 | 24 Nov 83 | 28 Jan 05 |  |
| D-85 | 8986 | 10 Dec 07 | 29 Dec 08 |  |
| Dome C II | 8989 | 12 Dec 95 | 12 Dec 95 |  |
| Cape Denison | 8988 | 20 Jan 90 | 17 Dec 99 |  |
| E-66 | 8912 | 12 Dec 07 | 12 Dec 07 |  |
| Byrd Station | 8903 | 05 Feb 80 | 05 Feb 80 |  |
| Mount Siple | 8981 | 20 Feb 92 | 20 Feb 92 |  |
| Theresa | 21358 | 29 Nov 94 | 29 Nov 94 |  |
| Brianna | 8931 | 30 Nov 94 | 15 Jan 02 |  |
| Harry | 8900 | 29 Nov 94 | 26 Jan 99 |  |
| Elizabeth | 21361 | 30 Nov 94 | 17 Jan 96 |  |
| Erin | 21363 | 29 Nov 94 | 18 Jan 96 |  |
| Siple Dome | 8938 | 21 Jan 97 | 24 Jan 99 |  |
| Swithinbank | 8927 | 18 Jan 97 | 01 Jan 08 |  |
| Kominko-Slade | 21364 | 13 Jan 06 | 26 Jan 09 |  |
| Marble Point | 8906 | 05 Feb 80 | 05 Feb 80 |  |
| Ferrell | 8929 | 10 Dec 80 | 09 Jan 01 |  |
| Pegasus North | 21357 | 23 Jan 90 | 03 Feb 00 | 11 Jan 09 |
|  | 21355 |  | 25 Jan 09 | 05 Feb 09 |
|  | 8923 |  | 05 Feb 09 | 06 Sep 09 |
|  | 8937 |  | 06 Sep 09 |  |
| Pegasus South | 8937 | 14 Jan 91 | 14 Jan 91 | 07 Jan 09 |
| Minna Bluff | 8939 | 22 Jan 91 | 22 Jan 04 |  |
| Linda | 8919 | 21 Jan 91 | 15 Jan 98 |  |
| Willie Field | 21364 | 25 Jan 92 | 29 Jan 01 | 11 Jan 09 |
|  | 30477 |  | 05 Feb 09 |  |
| Windless Bight | 8982 | 09 Dec 98 | 05 Feb 05 |  |
| Cape Bird | 8901 | 28 Jan 99 | 28 Jan 99 |  |
| Laurie II | 21360 | 01 Feb 00 | 16 Jan 01 |  |
| Lorne | 21356 | 12 Jan 07 | 12 Jan 07 |  |
| Mulock | 8907 | 24 Oct 06 | 24 Oct 06 |  |
| Mt. Fleming | 30393 | 01 Nov 06 | 01 Nov 06 |  |
| Possession Island | 8984 | 29 Dec 92 | 29 Dec 92 |  |
| Manuela | 8905 | 06 Feb 84 | 15 Feb 87 |  |
| Marilyn | 8934 | 16 Jan 84 | 30 Jan 01 |  |
| Schwerdtfeger | 8913 | 24 Jan 85 | 22 Jan 93 |  |
| Gill | 8911 | 24 Jan 85 | 25 Jan 91 |  |
| Elaine | 21357 | 28 Jan 86 | 28 Jan 09 |  |
| Lettau | 8928 | 29 Jan 86 | 24 Jan 07 |  |
| Vito | 8695 | 03 Feb 04 | 22 Jan 05 |  |
| Emilia | 8980 | 31 Jan 04 | 29 Jan 07 |  |
| Carolyn | 8722 | 02 Feb 05 | 02 Feb 05 |  |
| Mary | 8983 | 31 Jan 05 | 31 Jan 05 |  |
| Eric | 8697 | 29 Jan 05 | 29 Jan 05 |  |
| Margaret | 8910 | 12 Nov 08 | 12 Nov 08 |  |
| Larsen Ice Shelf | 8926 | 07 Feb 83 | 01 Jan 86 |  |
| Butler Island | 8902 | 01 Mar 86 | 01 Mar 86 |  |
| Fossil Bluff | 8920 | 10 Jan 05 | 10 Jan 05 |  |
| Limbert | 8925 | 30 Nov 95 | 30 Nov 95 |  |
| Bonaparte Point | 8921 | 05 Jan 92 | 14 Mar 08 |  |
| Sky-Blu | 8917 | 07 Feb 99 | 07 Feb 99 |  |
| Dismal Is. | 8932 | 27 May 01 | 27 May 01 |  |
| Hugo Island | 8935 | 10 Dec 94 | 02 Apr 09 |  |
| Henry | 8985 | 26 Jan 93 | 26 Jan 93 |  |
| Nico | 8924 | 26 Jan 93 | 26 Jan 93 |  |
| Mizuho | 21359 | 07 Oct 00 | 07 Oct 00 |  |
| Baldrick | 9116 | 01 Jan 08 | 01 Jan 08 |  |
| JASE2007 | 30305 | 27 Sep 07 | 27 Sep 07 |  |
| PANDA-South | 30416 | 14 Jan 08 | 14 Jan 08 |  |

4. AWS DATA SUMMARIES

The data received by the University of Wisconsin, Space Science and Engineering Center, contain all the information received by the ARGOS system including duplicate and erroneous transmissions.  Invalid data are eliminated during a quality check, and the valid data are converted to scientific units producing the complete data set.  Data selected at three hourly intervals, plus or minus forty minutes, produce a three hourly data set for each AWS unit month.  Section 6.1, AWS Performance, provides some explanations for missing and invalid data.

Use of the 2009 Antarctic AWS data for publication should acknowledge the support of NSF-OPP Grant 0636873 and 0944018 or reference this publication.

# 4.1.  Monthly Data Summaries

The monthly summaries consist of the monthly means, from the three hourly data set, and the extremes, from the complete data set.  For monthly values to be included, 25% of the three hourly observations must be available.  Months with 50-75% of data missing occur most often when a station is started or stopped in the middle of the month.  This can cause a bias in the monthly mean, especially during seasons when parameters such as temperature change rapidly.  Annual means are calculated only when twelve months of data are available.  The data are presented in the same order as the sites listed in Table 3.1.  Definitions of the monthly data summary headings are listed below.

Heading                                                Definition

Mean air temperature, oC.	Mean value for the month.

Percent of monthly data missing.        Ratio of the number of missing observations to the number of

possible observations X 100.

Maximum air temperature, oC.	Maximum value for the month.

Minimum air temperature, oC.	Minimum value for the month.

Mean wind speed, m/s.             	Mean value for the month.

Percent of monthly data missing.	Ratio of the number of missing observations to the number of

possible observations X 100.

Resultant wind speed, dir/vv.	Resultant speed and direction for the month.

Constancy.                  	Ratio of the monthly resultant to the monthly mean wind speed.

Maximum wind speed, dir/vv.	Maximum wind speed and direction for the month.

Mean air pressure, mb.	Mean value for the month.

Percent of monthly data missing         Ratio of the number of missing observations to the number of

possible observations X 100.

Maximum air pressure, mb.	Maximum value for the month.

Minimum air pressure, mb.	Minimum value for the month.

Potential temperature, K                     Mean value for the month.

4.2. Three Hourly Data Summaries

After the data are received from Service ARGOS, ten minute interval data are made available for each AWS unit. The data are calibrated for the individual station instruments with only gross error checking performed. This data set is created for those users who need fairly current information. These data are available by anonymous FTP (see Section 8). The ten minute data set for each AWS unit for the month is scanned to pick out the nearest observation within forty minutes of the UTC hours 00, 03, 06, 09, 12, 15, 18, and 21 to produce the three hourly data set. If valid data are not available within forty minutes of the three hourly time interval, then the entry is left blank to indicate missing data. The means, standard deviations, resultant wind speed and direction, the distribution of temperature, and wind speed with wind direction are determined from the three hourly observations and are presented as a monthly summary at the bottom of each page. A wind direction value of zero indicates a wind speed less than 0.50 m s-1.  North is indicated by a value of 360 degrees. The maximum and minimum values are taken from the complete ten minute data set, not the three hourly data set. The appropriate monthly data from the three hourly data set are used for the monthly summaries presented in Section 4.1. In the presence of sunlight the air temperatures are questionable if the wind speed is less than 1 m s-1. These summaries are available by anonymous FTP (see Section 8).

5.  AWS CALIBRATION

# 5.1. Temperature

The external and internal temperatures are calibrated using a 1000 ohm 0.05% resistor in place of the platinum resistance thermometers (PRT) with 1000 ohms resistance at 0oC.  Because the other resistances in the temperature circuit are known only to 1%, the temperature calibration will vary from one electronic unit to another.  The correction factor determined from the calibration resistor is programmed into the read-only-memories for each unit.  After the correction factors have been programmed into the AWS, a calibration box with 0.1% resistors is used to check the temperature calibration.  Resolution for AWS2B versions of AWS is 0.125 deg C with an accuracy of 0.25 deg C from -75.0 C to 0.0 C.  For AWS using CR10X or CR1000, the PRTs used are within the same +/- 0.25C.

# 5.2. Pressure

The atmospheric pressure transducer is a Parascientific model 215A Digiquartz( pressure gauge.  The transducer frequency changes from a nominal 40 kHz at zero pressure to a nominal 36 kHz at 1000 hPa. The pressure resolution is about 0.05 hPa.

Paulin aneroid barometers calibrated against a mercury barometer of 10 mm bore are used to check the pressure gauge calibration.  Comparisons are made between AWS units, a Parascientific Model 760-16B accurate to +/- 0.1 hPa, and with the mercury barometers at McMurdo Station, Antarctica.  The calibrations should be within +/- 0.2 hPa.

The reference vacuum on the older pressure transducers can degrade with time with a maximum observed 4 hPa shift to lower pressure after fifteen years. Recalibration of each pressure transducer would be desirable when each unit is serviced.

# 5.3. Wind direction and Speed

The Belfort model 123 aerovane (which is being phased out as a standard wind sensor) measures wind direction and speed.  The aerovane rotates a potentiometer wiper, and the fraction of full scale of the potentiometer is measured.  The wind direction is checked by positioning the aerovane to the cardinal directions relative to the boom supporting the aerovane.  North or the potentiometer zero is towards the antenna on the boom and has a maximum dead zone of 3o.  During the field installation, the boom is usually aligned along the north-south line as determined from the sun's azimuth, longitude, and Greenwich Mean Time.  In some cases the 180o end of the boom may point in a direction other than south.  At Manuela AWS site, the 180o end of the boom points up the glacier and a correction is added to the data during processing.  At Byrd AWS site the wind is usually out of the north so the boom was rotated 120o and the correction added during the data processing.  The wind speed is determined from the aerovane tachometer voltage output as 0.0472 volt per meter per second.  The aerovane tachometers are spun at 1800 rpm with a load of 1071.5 ohms, and the output should be 9.20 +/-0.05 vdc.

Additional wind sensors were used with AWS units for 2009.  These were the R.M. Young wind monitor model 05103 and the Hydro-Tech WS-3 anemometer with the WP-3 aerovane.  The Hydro-Tech system was used for measuring wind speed in the Adelie Coast area as well as Minna Bluff and Mulock AWS sites. The Hydro-Tech WS-3 is a disk rotor, 3 in. high and 12 in. overall diameter, with radial cups, and the threshold sensitivity is 3 mph.  The anemometer utilizes a commercial dc tachometer generator.  Output is 0 to +5 vdc (and 0 to 1 ma) over the desired full scale wind speed of 85 m/s.  Accuracy is +/- 2%.

The R.M. Young monitor 05103 also used a 10,000 ohm potentiometer with a 3o dead zone so that the wind direction was recorded identically with the Belfort/Bendix aerovanes.  The wind speed was from the range of 0 to 1.0 volt full scale corresponding to 50 m/s.  Thus the calibration for wind speed was a nominal .195 m/s/bit for the R.M. Young with +/- 1% up to 50 m/s.

# 5.4. Relative Humidity

The Vaisala HMP-35A/45D humidity sensor output voltage varies linearly with relative humidity (U).  The sensor is calibrated by placing it over saturated salt solutions with known relative humidities at room temperature:  sodium chloride (U=75%), and lithium chloride (U=12%) are used.  In addition, a dry inert gas, forced past the sensor, gives a 0% U, and the sensor output can be zeroed.  Then, the gain setting can be set directly using a salt solution with a high relative humidity, such as sodium chloride.  The resolution of the humidity sensor is about 1% and the drift is 2 to 3% per year in the field.  The relative humidity data are not included on the summary pages but are included in the 3 hourly data sets.

# 5.5. Vertical Air Temperature Difference

Two junction thermocouples are used to measure the air temperature difference between 3 m and 0.5 m on the tower.  The output is about 78 microvolts for 1oC temperature difference between the junctions at 0.0oC, dropping to 60 microvolts at -80oC.  Zero output is adjusted to 0.4 volts, so that 0 to 1 volt corresponds to a -6oC to +9oC range of air temperature differences between 3 m and 0.5 m.  The resolution is 0.05oC.  Calibration of the individual systems is done by applying known voltages to the amplifier input. The vertical temperature difference data are not included on the summary pages but are included in the 3 hourly data sets.

In addition some stations will have an additional platinum resistance thermometer (PRT) at a nominal 50 cm height above the snow surface.   The temperature difference with the standard Air Temperature PRT is output on the AWS2B versions of AWS while that actual “”lower temperature” is output on AWS using CR10X or CR1000 dataloggers.  For AWS2B the matched PRT’s will yield a +/- 0.25 degree C accuracy for the temperature difference.

5.6 Acoustic Depth Gauge

Acoustic depth gauges (ADG) were added to several stations as part of a study on precipitation. The gauges measure the distance to the surface with sonar pulses, with any change in distance indicating accumulation or depletion at the snow surface. The ADG used on the stations is a Campbell Scientific #SR50 and its successor the SR50A, with a resolution of 0.0001 m and an accuracy of +/- 0.01 m. The data was either transmitted real time or stored on a data logger onboard the station.

# 6.  AWS OPERATIONS SUMMARY FOR 2009

# 6.1.  AWS Performance

Fifty-five AWS units were operational for the 2009 year.  Based on the installation months, the AWS units delivered 94% of the temperature dat a, 91% of the pressure data and 80% of the wind data during 2009. Complete data sets of temperature, pressure, and wind data were received from 21 AWS units and 45 AWS units operated for the installed period. Ten AWS units were not received for one month or more during the year or stopped during the year.  Some of the stations were not received during the winter months due to low battery voltage.

The wind system has the poorest performance. If the wind speed is zero or the wind direction is constant for extended periods (days to months) then the data is considered invalid. The reason for this behavior is not known but is believed to be due to the buildup of rime or ice on the wind system. This usually occurs in the winter season and at several AWS sites. The wind speed is usually quite low or zero when the wind direction is constant.

Site	Performance

D-10 	OK.

D-47	Station stopped transmitting 18 January and began again 10 February. No relative humidity or delta-T sensors.

D-85	Station stopped transmitting 21 January and began again 01 February. Some missing transmissions in July and August.

Dome C II	OK. Some missing transmissions in July.

Cape Denison	Station transmitted erratically in March, May, June, and July. Aerovane failed 13 May so pressure not corrected for high wind speed conditions after that time.  Station stopped transmitting 25 July and began again 18 December.

E-66	Station transmitted erratically until November.

Byrd	Aerovane “frozen” most of March through December.

Mount Siple	Site has a "dog house" AWS without wind speed and direction. Station transmitted erratically in April and stopped 26 April. Station started transmitting erratically again in September. Batteries are old and don’t hold a charge through the winter.

Theresa			Station stopped transmitting 18 July and resumed 11 August.

Elizabeth			Aerovane "frozen" from May through the first part of November.

Brianna	Aerovane "frozen" from June through the first part of November. Pressure not functioning properly from October through the first part of November.

Harry	The aerovane was "frozen" occasionally from June through November.

Erin	The station stopped transmitting 12 August and resumed erratically transmitting in September.

Siple Dome	Aerovane “frozen” occasionally from May through October. Delta-T sensor not installed. Problems with temperature sensor.

Swithinbank		Pressure removed due to calibration problems.

Kominko-Slade	New station installed 27 January. Aerovane occasionally frozen May, June, September, and October and all of July and August.

Marble Point		OK.

Ferrell			OK.

Pegasus North	Station was removed 7 January. Replacement station put in on 25 January and worked only one day. Station replace again on 5 February, but problems appeared with pressure readings and wind measurements. Station replaced again on 7 September. Pressure problems were corrected, but the aerovane clamp was loose so the wind direction is questionable.

Pegasus South	Station was removed 7 January.

Minna Bluff	Aerovane “frozen” last half of April.

Linda			Station repaired 22 January.

Willie Field	Station removed 12 January. New station installed 5 February. Pressure calibration is incorrect because a different sensor was installed. The calibrations will have to be redone and the data rerun to restore the pressure measurements. The aerovane clamp was loose so the wind direction was deemed incorrect and removed from June through December.

Windless Bight		Occasional missing transmissions from May through September.

Cape Bird			OK.

Laurie II	Aerovane occasionally "frozen" in October.

Lorne	Aerovane occasionally "frozen" from April through October.

Mulock	Aerovane occasionally "frozen" in April. Station stopped 4 July.

Mt. Fleming	OK.

Possession Island	Site has a "dog house" AWS without wind speed and direction. Occasional missing transmission in July through September due to low battery voltage.

Manuela			Aerovane broken last half of April through December.

Marilyn	Aerovane occasionally "frozen" January and February and not functioning March through December.

Schwerdtfeger	Pressure jumps in June.

Gill	Relative humidity sensor not functioning. Aerovane “frozen” occasionally in April and May, July and August, and October.

Lettau	Station replaced 2 February.

Elaine			Station replaced 28 January. Station stopped transmitting 3 February.

Vito			Aerovane occasionally "frozen" June and July.

Emilia	Aerovane occasionally "frozen” May through September. Problems with the temperature sensor in January.

Carolyn	Transmissions erratic in May, June, August, and September.

Mary	Transmissions erratic in May through September.

Eric	Pressure data missing occasionally May through September.

Margaret	Aerovane occasionally "frozen” April through September.

Larsen Ice Shelf		OK.

Butler Island	OK.

Fossil Bluff		Some gaps in transmission in July and November.

Limbert	Aerovane not functioning June through most of September.

Bonaparte Point	Water temperature sensor not functioning after July. Pressure erratic in January.

Sky Blu			OK.

Dismal Island	Aerovane not functioning properly. Erratic transmissions from March through July.

Hugo Island	New station installed 2 February. Pressure sensor not functioning properly from August through December.

Henry	OK.

Nico			Aerovane occasionally "frozen" in September and October.

Mizuho	No relative humidity or delta-T sensors. A few gaps in transmission during August. Aerovane occasionally "frozen" in June and August.

Baldrick	Some pressure errors in January. Aerovane occasionally "frozen" in July through October.

JASE2007	Aerovane occasionally "frozen" in May through November.

PANDA-South	Transmitted erratically March through May. Station stopped transmitting 1 May and resumed 29 October.

# AWS Antarctic Field Activities

# The field team for the second half of the 2008-2009 field season was composed of Matthew Lazzara and Shelley Knuth from the University of Wisconsin-Madison and John Cassano and Melissa Richards from the University of Colorado-Boulder along with personnel from McMurdo Station, Ken Borek Twin Otter Pilots, and personnel from the WAIS Divide field camp. Assistance is also provided by personnel from the French Antarctic Program (Institut Polaire Francais – Paul Emile Victor, IPEV), the British Antarctic Survey (BAS), the Japanese Antarctic Research Expedition (JARE) and the Chinese National Antarctic Research Expedition (CHINARE).

# McMurdo area

On 7 January Pegasus South (8937) was removed. The next day 8 January the Iridium AWS at Willie Field was removed. Pegasus North was visited on 11 January and AWS unit 21357 was replaced with 21355. This unit only worked for three days. Willie Field was visited on the same day, and AWS unit 21364 was removed. On 16 January members of the field team visited Linda site (21362). One of the prongs of the antenna was broken, so a return trip had to be made on 21 January to replace the antenna. Ferrell site (8929) was also visited on 16 January to download the ADG data stored on the datalogger.

Pegasus North was revisited on 5 February, and AWS ID 8923 was installed. The pressure and wind speed did not work on this unit. Willie Field was also visited on 5 February, and ID 30477 was installed. The pressure will have to be recalibrated because a different pressure sensor was installed than the one the unit was calibrated for. Pegasus North was again visited on 7 September at the beginning of the 2009-2010 field season, and AWS ID 8937 was installed.

Ross Ice Shelf

Marilyn site (8934) was visited on 23 January. The site was buried so a new tower section was added. Carolyn site (8722) was also visited on this trip, and the electronics box was moved higher on the tower. On 24 January Vito site (8695) was visited. Another tower section was added, and the shaft holding the RM Young windbird was found to be loose. The clamp was tightened. Emilia (8980) was also visited and a tower section added.

Elaine was visited on 28 January, and AWS ID 21357 was installed. A new tower section was also added. Lettau (8928) was visited on 2 February, and the electronics box was moved higher on the tower.

# West Antarctica

Shelley Knuth and Melissa Richards went to the WAIS Divide camp in West Antarctica. They replaced the Kominko-Slade AWS unit with ID 21364.

7.  GLOBAL TELECOMMUNICATIONS SYSTEM

The data from 28 Antarctic AWS units were entered into the Global Telecommunications System (GTS) during 2009. The data are collected by Service ARGOS. As soon as the data are received, Service ARGOS processes them and sends them on to the National Weather Service which distributes the data to the GTS.The data headers are:

# SMAA14 KARS YYGGgg

SIAA14 KARS YYGGgg

SNAA14 KARS YYGGgg

where S indicates surface, M is main observations (at 00, 06, 12, and 18 UT), I is intermediate observations (at 03, 09, 15, and 21 UT), and N is any other time. AA14 is for Antarctica, and KARS stands for the Largo receiving center (backup is LFPW for the center in Toulouse, France). YY indicates the day in the month, GG is the hour, and gg is the minutes. Table 3.1 contains the WMO identification number used by the GTS grouped according to their purpose and proximity where possible. The data for the stations that do not have a WMO number are sent out on the GTS as Synoptic Mobil messages, which are created by the British Antarctic Survey.

The University of Wisconsin-Madison is responsible for obtaining WMO numbers for AWS sites and for providing Service ARGOS with calibration information for processing the data. The main reason for getting the AWS data into the GTS is to make sure that the data are available in near real time for all organizations operating in Antarctica and for numerical weather prediction efforts.

# 8.  DATA AVAILABILITY

a) On-Line. The data from our Automatic Weather Stations are available by anonymous FTP and Web site:

ftp://amrc.ssec.wisc.edu

http://amrc.ssec.wisc.edu

The login is "anonymous" (do not use the quotation marks), and the password is your email address.  Once you have logged in, change to the pub/aws subdirectory.  A listing of our station locations, names, and ARGOS ID numbers is located in the file "biglist" in this subdirectory.  It is meant to serve as a guide to our stations as their ID numbers sometimes change. A complete guide for navigating the site may be found in the file “readme.faq”.

b) 3 hourly Observations. Our three-hourly interval data for Antarctica in ASCII text format are contained in the year subdirectories of pub/aws/antrdr.  The data have been corrected, i.e. an effort has been made to remove the bad data points.  These data take longer to process, so the data for the most recent month are not available in this format.  Within each of the year subdirectories of pub/aws/antrdr, there are text files named "3hrlist??" (where ?? indicates the last two digits of the year). These files list what station's data are contained in which files. The files “readme.updates?” in pub/aws/antrdr contain information on updates and/or corrections to the data, and the file “readme.3format” contains file name construction information and format of the three-hourly data.

c) Monthly Summary. The directory pub/aws/summary/monthly contains ASCII printable text files of the paper data summary sheets.  The format of the files can be found in the file "readme.sum" while updates and corrections to the data are located in "readme.sumupdates".  The data are located in year subdirectories of pub/aws/summary/monthly.

d) Ten Minute Observations. For those users who need more current information, we have made available 10 minute interval data in ASCII text format for each station.  These data are located in year subdirectories of pub/aws/10min/rdr.  The data have been calibrated for the individual station instruments, but no other corrections have been made.  The year subdirectories also contain a text file named "namelist??" (where ?? indicates the last two digits of the year in question).  These files list what station's data are contained in which files.

Several important readme files are located in pub/aws/10min/rdr. The file "readme.format" contains information on filename construction of the data, as well as well as file content and is a must for those unfamiliar with the data. The files "readme.updates?" contain important information on changes/additions to the data.

e) New Formats. In addition, we have begun to make available data for each station that has been quality controlled. The datasets are in 10 minute, 1 hour and 3 hour intervals. They can be found at pub/aws/q10, pub/aws/q1h, and pub/aws/q3h. Readme files in each directory will give the file formats. At this point, data are available for September, 2001 through February, 2003 and January, 2009 through June, 2010 for all stations. Selected stations are available for some of the other years.

f) Questions. Our site is available 24 hours a day, 7 days a week.  If you have questions or problems, send email to amrc@ssec.wisc.edu.  We can also be reached by phone at (608) 265-2209 or (608) 262-0436 or fax at (608) 262-5947.

By mail, please contact:

Linda M. Keller

945 Atmospheric, Oceanic, and Space Sciences Building

1225 W. Dayton St.

Madison, WI  53706

USA

# 9.  ACKNOWLEDGMENTS

This material is based upon work supported by the National Science Foundation, Office of Polar Programs Grant 0636873 and 0944018 under the management of Dr. Peter Milne. Assistance from the following countries is gratefully acknowledged. Expeditions Polaires Francaises installs and maintains the AWS units from the Adelie Coast to Dome C II.  The British Antarctic Survey maintains the AWS units on the east side of the Antarctic Peninsula and south of Adelaide Island. The Japanese Antarctic Research Expedition (JARE) installs and maintains the AWS units at Relay Station, Mizuho, Dome Fuji, and JASE2007. The Chinese National Antarctic Research Expedition (CHINARE) installs and maintains the AWS unit at PANDA-South. The Mawson’s Hut Foundation maintains the AWS unit at Cape Denison.

Mary R. Albert	Prof. Richard Alley	Dr. I. Allison

Thayer School of Engineering	The Pennsylvania State University	Antarctic CRC

University of New Hampshire	Earth Systems Science Center	University of Tasmania

MacLean ESC Rm M215	306 Deike Building	Hobart, Tasmania  7001

Hanover, NH  03755	University Park, PA  16802	AUSTRALIA

Dr. Sridhar Anandakrishnan	Dr. Jean-Claude Andre	Stefania Argentini

The Pennsylvania State University	Centre National de Recherches	Istituto di Scienze dell' Atmosfera e

Earth Systems Science Center	Meteorologiques	del Clima

540 Deike Building	42 Avenue G. Coriolis	Consiglio Nazionale delle Ricerche

University Park, PA  16802	F-31057 Toulouse Cedex	Via del Fosso del Cavaliere, 100

FRANCE	00133 Roma

ITALY

Dr. Gail Ashley	Liana Bacigalupi	Dr. Karen S. Baker

Rutgers University	Library	Scripps Institute of Oceanography

Dept. of Geological Sciences	ENEA Progetto Antartide	UCSD - A - 018

Piscataway, NJ  08854	Via Anguillarese, 301	La Jolla, CA  92093

00060 S. Maria di Galeria (Roma)

ITALY

Prof. Roger Bales	Dr. L.A. Barrie	Ian J. Barton

University of California-Merced	Atmospheric Environment Service	CSIRO Marine Laboratories

P.O. Box 2039	4905 Dufferin Street	GPO Box 1538

Merced, CA  95344	North York, Ontario	Hobart, Tasmania 7001

M3H 5T4	AUSTRALIA

CANADA

Rabindra Basnyat	Rob Bauer	Ms. Judy Bausch

General Post Office	NSIDC/CIRES	Yerkes Observatory

P.O. Box #6644	University of Colorado	P.O. Box 258

Kathmandu	Boulder, CO  80309-0449	Williams Bay, WI  53191

NEPAL

Dr. John Bengston	Prof. Charles R. Bentley	Biblioteca Y Centro de

NOAA/NMFS	University of Wisconsin	Dir. Meteorologica de Chile

National Marine Mammal Lab.	Geophys. & Polar Research Cen.	Casilla 717

7600 Sand Pt. Way N.E.	1215 W. Dayton St.	Santiago

Seattle, WA  98115-0070	Madison, WI  53706	CHILE

Dr. Robert Bindshadler	Prof. Krzystztof Birkenmajer, Chrm.	Dr. George Blaisdell

NASA	Com. On Polar Res., Polish Academy 	National Science Foundation

Goddard Space Flight Center	of Sciences	Office of Polar Programs

Code 971	Dept. of Dynamic Geology	Room 755

Greenbelt, MD  20771	Instit. of Geological Sciences	4201 Wilson Blvd.

ul. Senacka 1-3 31-002 Krakow	Arlingtion, VA 22230

POLAND

Mr. Greg Bodeker	Dr. John Bolzan	Dr. Scott Borg

University of Natal	Ohio State University	National Science Foundation

Space Physics Research Instit.	Byrd Polar Research Center	Office of Polar Programs

King George V. Ave.	1090 Carmack Road	Room 755

Durban 4001	Columbus, OH  43210-1002	4201 Wilson Blvd.

SOUTH AFRICA	Arlington, VA  22230

Irina I. Borzenkova	Prof. David Braaten	John W. Briggs, Engineer

State Hydrological Institute	University of Kansas	Yerkes Observatory

23 Second Line	Dept. of Physics and Astronomy	373 West Geneva Street

199053, St. Petersburg	Lawrence, KS  66045	Williams Bay, WI  53191-0258

RUSSIA

Dr. David Bromwich	Neva Brown	Giancarlo Caimi

Ohio State University	30 Lantern Lane	Via S. Benelli 8

Byrd Polar Research Center	Wrentham, MA  02093	20151

1090 Carmack Road	Milano

Columbus, OH  43210-1002	ITALY

Prof. Azzio Caneva	Captain, R/V Lawrence G. Gould	Captain, R/V Nathaniel B. Palmer

Universita di Genova	c/o AGUNSA	c/o AGUNSA

Stazione Geofisica	Deposito Franco Antarctico	Deposito Franco Antarctico

12080 Roburent	Av. Independencia 772	Av. Independencia 772

Cuneo	P.O. Box 60-D Punta Arenas	P.O. Box 60-D Punta Arenas

ITALY	CHILE	CHILE

Dr. A.M. Carleton	Michael Carmody	Prof. John Carroll

Dept. of Geography	Raytheon Polar Services	University of California

The Pennsylvania State University	7400 South Tuscon Way	Dept. LAWR

0314 Walker Building	Centennial, CO 80112-3938	Davis, CA  95616

University Park, PA  16802

I.F.S. Cavalacanti	Art Cayette	Roberto Cervellati

Depto Meteorologia, INPE	SPAWAR System Center	ENEA Pas Progetto Antarctide

Caixu Postal 515	P.O. Box 190022	S.S. Anguillarese 301

12 200 Sao Jose dos Campos	North Charleston, NC  29419-9022	Roma

Sao Paulo	ITALY

BRAZIL

Prof. Chen Liqi, Director	Dr. K.Y. Chen	Pecheng Chu

Chinese Antarctic Administration	University of Florida	Naval Postgrad. School, Code OC/CU

No. 1 Fuxingmenwai Street	Dept. of Astronomy	Dept. of Oceanography

Beijing	211 Space Sci. Research Building	Monterey, CA  93943

CHINA	Gainesville, FL  32611

William Colston	Dr. Josefino C. Comiso	The Committee on Antarctic Research

National Science Foundation	NASA/Goddard Space Flight Center	ul. Vavilova, 44

Office of Polar Programs	Code 971	Building 2

Room 755	Greenbelt, MD  20771	Moscow 117333

4201 Wilson Blvd.	RUSSIA

Arlington, VA  22230

Jessie Crain	Richard Cram	Dick Crouthamel

National Science Foundation	Federal Building	National Weather Service

Office of Polar Programs	National Climatic Data Center	Mail Code W/OM31

Room 755	Asheville, NC  28801	1325 E-W Highway

4201 Wilson Blvd.	Silver Spring, MD  20910

Arlington, VA 22230

CRREL-TL	W. Darnell	Dr. Thomas DeFelice

Dept. of the Army Corps of Engineers	NASA, Langley Research Center	University of Wisconsin

Hanover, NH  03755-1290	Mail Stop 185	Dept. of Geoscience, Lapham Hall

Hampton, VA  23665-5225	P.O. Box 413

Milwaukee, WI  53201

Rear Ar. Fernando M. Diegues, Sec.	Debra Diemand	Director

Comm. Interministerial para os 	CRREL-TL	Cold And Arid Regions

Recursos do Mar (CIRM)	Dept. of the Army Corps of Engineers	Environ. and Engineering Res.

Ministerio da Marinha	Hanover, NH  03755-1290	Academia Sinica

40 ANDAR	Lanzhou 730000

70055 DF-Brasilia	CHINA

BRAZIL

Dr. David J. Drewry	Dr. Hiroyuki Enomoto	Dr. Karl Erb

Vice-Chancellor	Kitami Institute of Technology	National Science Foundation

University of Hull	Koencho 165	Office of Polar Programs

Cottingham Road	Kitami, Hokkaido	Room 755

Hull, Yorksire HU6 7RX	090-8507  JAPAN	4201 Wilson Blvd.

UNITED KINGDOM	Arlington, VA  22230

Edelberto R. Farias, Director	Jane Ferrigno	Michel Fily

Dir. Meteorologica de Chile	USGS National Center	Lab. de Glaciologie et Geophys. de

Casilla 717-STGO	Mail Stop 927	L'Environnement

CHILE	Reston, VA  22092	BP 96

38402 Saint-Martin-d'Heres

FRANCE

Margaret Finger, Librarian	Dr. Joan Fitzpatrick	Dr. Joseph Fletcher

University of Melbourne	Federal Center	NOAA/ERL R/E

Dept. of Meteorology	U.S. Geological Survey-Denver	325 Broadway

Parkville, Victoria  3052	P.O. Box 25046	Boulder, CO 80303

AUSTRALIA	Denver, CO  80225

Dr. R.J. Flint	Dr. Benson Fogle	Prof. Theodore D. Foster

185 Bear Gulch Road	12709 Glen Mill Rd.	Scripps Institute of Oceanography

Woodside, CA  94062	Potomac, MD  20854	Mail Code 0240

University of California, San Diego

LaJolla, CA  92093-0240

Andrew G. Fountain	Prof. H. Fukunishi	Gen. Ricardo Galarza

Dept. of Geology	Tohoku University	Uruguayan Antarctic Institute

Portland State University	Upper Atmos. & Space Research 	Buenos Aires 350

P.O. Box 751	Laboratory	Montevideo

Portland, OR 97207-0751	Sendai 980-0845	URUGUAY

JAPAN

Christophe Genthon	Abbate Giulia	Hector R. Godoy

Lab. de Glaciol. et Geophys. de l'Env.	ENEA Casaccia	Servicio Meteorologico National

54 Rue Moliere, DU BP 96	Italian Antarctic Project	Depto Antarctico

F-38402 Saint Martin d'Heres	Via Anguillarese 301	25 de Mayo 658

Cedex	00100 Roma	Capital Federal

FRANCE	ITALY	REPUBLICA ARGENTINA

Goldthwait Polar Library	Dr. Shulamit Gordon	Robert Grumbine

Byrd Polar Research Center	Antarctica New Zealand	5200 Auth Rd., Room 204

Ohio State University	Private Bag 4745	W/NMC21

1090 Carmack Road	Christchurch	Camp Springs, MD 20746

Columbus, OH  43210-1002	NEW ZEALAND

Ritva Hanninen, Librarian	Inger Hanssen-Bauer	Ross Harp, Jr.

Finnish Meteorological Institute	Norwegian Meteorological Institute	P.O. Box 1717

Box 503	P.O. Box 43 - Blindem	Boulder, CO 80306

SF-00101 Helsinki 10	0313 Oslo 3

FINLAND	NORWAY

Ralph Harvey	G. Hernandez	Dr. Roger Hewitt

Dept. Geological Sciences	University of Washington	Southwest Fisheries Center

Case Western Reserve University	Geophysics Program	Antarctic Ecosys. Research Gr.

112 A.W. Smith	AK-50	P.O. Box 271

10900 Euclid Ave.	Seattle, WA  98195	La Jolla, CA  92038

Cleveland, OH  44106-7216

Dr. Austin Hogan	Hugh Hutchinson	Lloyd E. Irwin

P.O. Box 21	Bureau of Meteorology	NOAA, NWS

Piermont, NH  03779-0021	20 Ellerslie Rd.	SSMC2, Station 5118

Hobart, TAS  7000	1325 East-West Highway

AUSTRALIA	Silver Spring, MD  20910

Alexandra Isern	T.H. Jacka	Dr. Stanley Jacobs

National Science Foundation	Antarctic CRC	Columbia University

Office of Polar Programs	Box 252C	Lamont Observatory

Room 755	Hobart, Tasmania	Palisades, NY  10964

4201 Wilson Blvd.	AUSTRALIA 7001

Arlington, VA  22230

Martin Jeffries	Dr. Ken Jezek	Prof. Jia Pengqun

University of Alaska	Ohio State University	Polar Met. Lab., Acad. of Met. Sci.

Geophysical Institute	Byrd Polar Research Center	State Meteorological Admin.

903 Koyukuk Ave.	1090 Carmack Road	Baishiqiaolu No. 46, West Suburb

Fairbanks, AK  99705-7320	Columbus, OH  43210-1002	Beijing,  100081

CHINA

P.D. Jones	Prof. Anders Karlqvist, Director	Stephen J. Katz

University of East Anglia	Royal Swedish Academy of Science	Colorado School of Mines

Climate Research Unit	Polar Research Secretariat	Arthur Lakes Library/Serials

Norwich NR4 7TJ	Box 50005	Golden, CO  80401

UNITED KINGDOM	10405 Stockholm

SWEDEN

Chris Kidd	Dr. Tokio Kikuchi	Dr. John C. King

School of Geography	Kochi University	British Antarctic Survey

University of Birmingham	Dept. of Physics, Faculty of Sci.	High Cross, Madingley Road

Edgbaston, Birmingham	2-5-1, Akebono-cho	Cambridge CB3 OET

B15 2TT	Kochi 780-8072	UNITED KINGDOM

UNITED KINGDOM	JAPAN

Akio Kitoh	Dr. Yuji Kodama	Dr. K.Ya Kondratyev

Meteorological Research Institute	Hokkaido University	The USSR Acad. Inst. for Lake Res.

Climate Research Division	Institute of Low Temp. Science	Sevastyanov Str., 9

Tsukuba, Ibaraki 305-0052	Sapporo 060-0819	St. Petersburg,  196199

JAPAN	JAPAN	RUSSIA

Dr. Els Kooij-Connally	Prof. Dr. Christopher Kottmeier	Dr. Steve Kottmeier

Library ECMWF	Universitat Karlsruhe	Raytheon Polar Services

Shinfield Park	Institut fur Meteorologie und 	7400 South Tuscon Way

Reading, Berkshire RG2 9AX	Kaiserstr. 12 (Physikhochhaus)	Centennial, CO  80112-3938

UNITED KINGDOM	76128 Karlsruhe

GERMANY

Prof. Dr. H. Kraus	Dr. Monica Kristensen	Arlin Krueger

Met. Institut der Universitat Bonn	Norwegian Meteorological Institute	NASA/Goddard Space Flight Center

D-5300 Bonn 1	Postboks Box 43 Blindem	Code 616

FRG Auf Dem Hugel 20	0313 Oslo 3	Greenbelt, MD  20771

GERMANY	NORWAY

Dr. B.L. Krutskikh	Prof. M. Kuhn	Dr. Ron Kwok

Arctic & Antarc. Research Institute	Universitat Innsbruck	Senior Research Scientist

St. Petersburg,  191104	Institut fur Met. & Geophysik	Jet Propulsion Laboratory

RUSSIA	Innrain 52	California Institute of Technology

A-6020 Innsbruck	4800 Oak Grove Dr.

AUSTRIA	Pasadena, CA 91109

Dr. Victor Lagun	Claude M. Laird	Anthony Lazzara

Air-Sea Interaction Dept.	University of Kansas	P.O. Box 72

The Arctic & Antarc. Scientific Res. 	2291 Irving Hill Drive	Morgan, VT  05853

38 Bering Street	Campus West

199 397 St. Petersburg	Lawrence, KS  66045

RUSSIAN FEDERATION

Brig. Gen. Jorge E. Leal	Bang Yong Lee	Denyse Lemaire-Ronveaux

Dir. Nacional del Antarctico	Korea Ocean Research & Dev. Instit.	Dept. des Sci. de la terre et de

Cerrito 1248	Polar Research Center	Faculte des Sciences

1010 Buenos Aires	Ansan P.O. Box 29	CP 160 Ave F.D. Roosevelt, 50

ARGENTINA	Seoul 425-600	1050 Brussels

SOUTH KOREA	BELGIUM

Dr. Marc Lessard	Librarian	Librarian

Morse Hall	Australian Antarctic Division	British Antarctic Survey

University of New Hampshire	Channel Highway	High Cross, Madingley Road

8 College Rd.	Kingston, Tasmania  7050	Cambridge CB3 OET

Durham, NH  03824-2600	AUSTRALIA	UNITED KINGDOM

Library	Library	Library

Alfred Wegener Inst. fur Polar und 	Antarctica New Zealand	Climatic Research Unit

Meeresforschung	Private Bag 4745	University of East Anglia

Forschungsstelle Potsdam	Christchurch	Norwich NR4 7TJ

Telegraphenberg A 43	NEW ZEALAND	UNITED KINGDOM

14473 Potsdam

GERMANY

CRREL Library	Keith B. Mather Library	Library

Attn: Elisabeth Smallidge	Geophysical Institute/IARC	National Inst. of Polar Research

72 Lyme Road	903 Koyukuk	10-3

Hanover, NH  03755-1290	Fairbanks, AK 99775	Midoricho

Tokyo 173-8518

JAPAN

Library	Michael P. Lizotte	Dr. C. Lorius

Tasmania/Antarctica Reg. Office	800 Algoma Blvd.	C.R.N.S., Lab. de Glaciol. et

Bureau of Meteorology	Oshkosh, WI  54901	Geophys. de L'Environ.

GPO Box 727G	rue Moliere, BP 96

Hobart, Tasmania 7001	38 402 Saint Martin D'Heres

AUSTRALIA	Cedex

FRANCE

Dr. Douglas H. Lowenthal	Daren Lu	Prof. Lu Longhua

Desert Research Institute	Institute of Atmospheric Physics	Polar Meteorology Research Lab.

2215 Raggio Parkway	CAS	Acad. of Met. Sci., State

Reno, NV  89512-1095	Beijing 100029	Meteorological Admin.

CHINA	Baishiqiaolu #46, West Suburb

Beijing 100081

CHINA

Dan Lubin	Kirk A. Maasch	Doug MacAyeal

UCSD/SIO	Quaternary Institute	Dept. of Geophysical Sciences

La Jolla, CA  92093-0221	University of Maine	5734 S. Ellis Ave.

5711 Boardman Hall	Chicago, IL  60637

Orono, ME  04469-5711

Manager, Laboratory Science	Manager, Science Support	Dr. M.J. Manton

Raytheon Polar Services Company	Palmer Station	Bureau of Meteorology Research

McMurdo Station	Raytheon Polar Services Company	GPO Box 1289K

PSC 469 Box 700	7400 South Tucson Way	Melbourne, Victoria 3001

APO, AP 96599-1035	Centennial, CO  80112	AUSTRALIA

Dominique Marbouty	Cristine Coutinho Marcial	Alberto Marenga

European Cent. for Med Range 	Sec. Da Com. Intermin., Para 	Polar Documentation Centre

Weather Forecasts	Recursos do Mar.	P.O. Box 14002

Shinfield Park, Reading	Min. da Marinha, SECIRM-40 ANDAR	00149 Roma, (Trullo)

Berkshire RG2 9AX	Cep: 70055-Brasilia-D.F.	ITALY

UNITED KINGDOM	BRAZIL

Roberta Marinello	Paul Mayewski	Viktor L. Mazo

National Science Foundation	Dept. of Geological Sciences	USSR Academy of Sciences

Office of Polar Programs	University of Maine	Institute of Geography

Room 755	5790 Bryand Global Sciences Center	29 Staromonetny

4201 Wilson Blvd.	Orono, ME  04469-5790	109017 Moscow

Arlington, VA  22230	RUSSIA

Dr. Joseph R. McConnell	Thomas McIntyre	Christopher P. McKay

Research Professor	F/PR, NOAA, NMFS	NASA, Solar Systems Explor. Branch

Division of Hydrological Sciences	1335 East West Highway	Ames Research Center

Desert Research Institute	Silver Spring, MD  20910	Moffett Field, CA  94034

2215 Raggio Parkway

Reno, NV 89512

Thomas K. Mefford	Meteorology Department Library	Meteorology Office

NOAA/ESRL/GMD	The Pennsylvania State University	McMurdo Station, Antarctica

325 Broadway	503 Walker Bldg.	PSC 469 Box 700

R/GMD1	University Park, PA  16802	APO AP  96599-5700

Boulder, CO  80305

Tony Meunier	Dr. Peter Milne	Dr. Kingtse C. Mo

USGS MS 515	National Science Foundation	NOAA/NWS

Reston, VA  20192	Office of Polar Programs	Nat. Meteorological Center

Room 755	Washington, D.C.  20233

4201 Wilson Blvd. Arlington, VA  22230

Al Mongeon	Prof. Joseph M. Moran	Dr. Richard E. Moritz

National Weather Service	UW-Green Bay	University of Washington

WMO Representative	Dept. of Earth Science	Polar Science Center

W/OSO 242	Green Bay, WI  54311	1013 N.E. 40th Street

1325 East West Highway	Seattle, WA  98015

Silver Spring, MD  20910

Robert Morse	Dr. Ellen Mosley-Thompson	Mr. G.B. Mukherji, Director

UW-Madison	Ohio State University	Dept. of Ocean Development

Dept. of Physics	Byrd Polar Research Center	Block 12 C.G.O. Complex

Room 3406 Sterling Hall	1090 Carmack Road	Lodi Road

475 N. Charter Street	Columbus, OH  43210-1002	New Delhi  110003

Madison, WI  53706	INDIA

Prof. Frank J. Murcray	John Nairn	M.R. Nayak

University of Denver	Bureau of Meteorology	National Institute of Oceanography

Dept. of Physics	Antarctic Met. Center	Marine Instrumentation Div.

Denver, CO  80208-0202	Project Development Center	N.I.O. Dona Paula

P.O. Box 1289K, Melbourne 3001 	Goa-403 004

AUSTRALIA	INDIA

National Center for Atmospheric 	William Neff	NOAA/MASC Library

NCAR Library - Serials	NOAA/ERL/WPL, R/E/WP7	Acquisitions MC5

P.O. Box 3000	325 Broadway	325 Broadway

Boulder, CO  80307	Boulder, CO  80303	Boulder, CO  80303

NSF Representative	Prof. H.J. Paech	Kathy Pagan

New Zealand	Academy of Sciences of the GDR	NASA/AMES

PSC 467 Box 296	Central Earth Physics Instit.	Mail Stop 245-5

APO AP 96531-2000	Telegrafenberg A 43	Moffett Field, CA  94035

E-1561 Potsdam

GERMANY

Dr. Julie Palais	Prof. Thomas Parish	Dr. Byong Kwon Park, Director

National Science Foundation	University of Wyoming	Korea Ocean Res. & Dev. Institute

Office of Polar Programs	Dept. of Atmospheric Sciences	An San P.O. Box 29

Room 755	P.O. Box 3038, Univ. Station	Seoul 425-600

4201 Wilson Blvd.	Laramie, WY  82071	SOUTH KOREA

Arlington, VA  22230

Carol H. Pease	Dr. Andrea Pellegrini	Dr. Polly Penhale

PMEL NOAA-Building 3	PAS/Progetto Antarctide	National Science Foundation

7600 Sand Point Way NE	ENEA-Casaccia	Office of Polar Programs

Seattle, WA  98115-0070	C.P. 2400	Room 755

00100 Roma A.D.	4201 Wilson Blvd.

ITALY	Arlington, VA  22230

Polar Research Center	Joseph Prejs	Dr. Tony Press, Director

Korean Ocean Research and Dev. Inst.	1501 S. Clifton Ave.	Antarctic Division

Ansan P.O. Box 29	Bloomington, IN  47401-6649	Channel Highway

Seoul 425-600	Kingston, Tasmania 7050

SOUTH KOREA	AUSTRALIA

Linda Preston, Librarian	Rajmund Przybylak	Dominique Raynaud

Federal Bldg.-Library	Nicholas Copernicus University	Laboratoire de Glaciol. et Geophys.

Nat. Climatic Data Center/NOAA	Dept. of Climatology	de l'Environ.

Asheville, NC  28801-2696	ul. Danielwskiego 6	BP 96 38402 St. Martin d'Heres

87-100 Torun	Cedex

POLAND	FRANCE

Margaret N. Rees	Ms. Winifred Reuning	David Reusch

University of Nevada	National Science Foundation	517 Deike Building

Dept. of Geophysics	Office of Polar Programs	Earth and Environmental Systems

Las Vegas, NV  89154	Room 755	Pennsylvania State University

4201 Wilson Blvd.	University Park, PA  16802

Arlington, VA  22230

Dr. Carlos A. Rinaldi, Director	Dr. Ted J. Rosenburg	Dr. Thomas F. Ross

Instituto Antarctico	University of Maryland	NOAA/NCDC

Cerrito 1248	Inst. for Phys. Sci. & Tech.	National Climatic Data Center

1010 Buenos Aires	College Park, MD  20742	Room 121

ARGENTINA	Federal Building

Asheville, NC  28801-2696

Comodoro Enrique Saavedra	Akhil Saxena, Section Officer	Ted Scambos

Servicio Meteorologico Nacional	Government of India	National Snow and Ice Data Center

25 de Mayo 658	Dept. of Ocean Development	University of Colorado

1002 Buenos Aires	Mahasagar Bhavan, Block-12	Campus Box 449

REPUBLICA ARGENTINA	CGO Complex, Lodi Road New Delhi 	Boulder, CO  80309-0449

110003

INDIA

Greg Scharfen	Guy Schayes	Thomas W. Schmidlin

National Snow and Ice Data Center	UCL-Institut d'Astron. et de Geophys.	Kent State University

University of Colorado	Chemin du Cyclotron 2	Dept. of Geography

Campus Box 449	B-1348 Louvain-La-Neuve	Kent, OH  44242

Boulder, CO  80309-0449	BELGIUM

Schwerdtfeger Library	Science & Technology Corp.	Science Library

Space Science and Engineering 	101 Research Drive	Amundsen-Scott South Pole Station,

1225 W. Dayton St., Room-317	Hampton, VA  23666	Antarctica

Madison, WI 53706	ATTN: C.A. Keen	c/o Inland Stations Manager

7400 South Tuscon Way

Centennial, CO 80112-3938

Science Library	Science Library	Service Central d'Explication

Crary Laboratory	Palmer Station, Antarctica	Division Climatologie

McMurdo Station, Antarctica	c/o Supervisor, Lab Operations	2, Division Rapp

c/o Laboratory Manager	7400 South Tuscon Way	75340 Paris Cedex 07

7400 South Tuscon Way	Centennial, CO 80112-3938	FRANCE

Centennial, CO 80112-3938

Dr. Alberto Setzer	Jonathan Shanklin	Dr. Hayley Shen

Instituto de Pesquisas Espaciais	British Antarctic Survey	Dept. of Civil and Environmental

Dept. de Meteorologia e 	High Cross, Madingley Road	Engineering

Caixa Postal 515	Cambridge CB3 OET	Clarkson University

12201-Sao Jose dos Campos-SP	UNITED KINGDOM	Potsdam, NY  13699-5710

BRAZIL

Madan L. Shrestha, Dir. General	Dr. Christopher A. Shuman	August L. Shumbera

Dept. of Hydrology & Meteorology	UMBC Goddard Earth Science and	Federal Building

P.O. Box No. 406	Technology Center	National Climatic Data Center

Babarmahal, Kathmandu	Planetary Geodynamics Branch	Asheville, NC  28801

NEPAL	Code 698

Greenbelt, MD 20771

Kim Silverman	Prof. Ian Simmonds	Prof. Raymond Smith

National Science Foundation	School of Earth Sciences	University of CA-Santa Barbara

Office of Polar Programs	University of Melbourne	Computer Systems Laboratory

Room 755	Parkville, Victoria	Santa Barbara, CA  93106

4201 Wilson Blvd.	AUSTRALIA 3052

Arlington, VA  22230

Dr. Philip M. Solomon	Dr. Susan Solomon	Dr. Roland Souchez

SUNY Stoneybrook	NOAA/Aeronomy Laboratory	Faculte des Sciences

Dept. of Physics	325 Broadway	Dept. des Sci. de la terre et de

Stoneybrook, NY  11794	Boulder, CO  80303	CP 160 Ave. F.D. Roosevelt, 50

1050 Brussels

BELGIUM

South Pole Station	Todd Sowers	Sharon Stammerjohn

PSC 468 Box 400	University of Rhode Island	Institute for Computational Earth

APO AP 96598-5400	URI/GSO S. Ferry Road	System Science

Narragansett, RI  02882-1197	UCSD

Sanata Barbara, CA 93106-3060

Station Manager	Towanda Street	Dr. N.A. Streten

Palmer Station, Antarctica	National Ice Center	Bureau of Meteorology

c/o AGUNSA	FOB#4, Room 2301	Box 1289 K, Melbourne 3000

Deposito Franco Antarctico	4251 Suitland Rd.	Victoria

Av. Independencia 772, P.O. Box 60-D	Washington, DC  20395	AUSTRALIA

Punta Arenas

CHILE

Dr. A.P. Sturman	Swedish Polar Research Secretariat, 	Dr. Charles Swithinbank

University of Canterbury	Box 50005	Home End Fulbourn

Dept. of Geography	S10405 Stockholm	Cambridge CB1 5BS

Christchurch 1	SWEDEN	UNITED KINGDOM

NEW ZEALAND

Tasmanian/Antarctic Reg. Office	Dr. Kendall Taylor	Dr. Calvin Teague

Bureau of Meteorology	Desert Research Institute	Center for Radar Astronomy

Hobart	P.O. Box 60220	Dept. of Electrical Engineering

AUSTRALIA	5625 Fox Ave.	Stanford University

Reno, NV  89506-0220	Stanford, CA  94305

Martha B. Thayer	Geza T. Thuronyi	Dr. Brian A. Tinsley, MSF022

NOAA Library	Library of Congress	University of Texas-Dallas

7600 Sand Point Way NE Bldg. 3	Science & Technology Division	Box 830688

Bin C-15700	Washington, D.C.  20540	Richardson, TX  75083-0688

Seattle, WA  98115

Dr. Adrian Tuck	John Turner	Dr. Rein Vaikmae

R/E/ALG	British Antarctic Survey	Estonian Academy of Science

NOAA/Aeronomy Lab	High Cross, Madingley Road	Institute of Geology

325 Broadway	Cambridge CB3 OET	7 Estonia Puiestee

Boulder, CO  80303	UNITED KINGDOM	200101 Tallinn

ESTONIA

Luca Valenziano	Rodolfo del Valle	Michiel van den Broeke

CNR-TESRE	Instituto Antarctico Argentino	IMAU

via P. Gobetti 101	Cerrito 1248-1010	P.O. Box 80005

I-40129	Buenos Aires	3508 TA Utrecht

Bologna	ARGENTINA	THE NETHERLANDS

ITALY

Dr. Harry van Loon	Michael Van Woert	E.D. Waddington

NCAR	National Science Foundation	University of Washington

P.O. Box 3000	Office of Polar Programs	Geophysics AK-50

Boulder, CO  80307	Room 755	Seattle, WA  98195-1650

4201 Wilson Blvd.

Arlington, VA  22230

Dr. Thomas Wagner	Von Walden	John E. Walsh

Cryosphere Program Manager	Dept. of Geography	University of Illinois

Earth Science Division	University of Idaho	Dept. of Atmospheric Sciences

NASA, HQ  Mail Suite 3F71	McClure Building, Room 203	1101 W. Springfield Ave.

Washington, DC  20546	Moscow, ID  83844-3021	Urbana, IL  61801

Stephen G. Warren	Dr. Gerd Wendler	Prof. G. Wojcik

University of Washington	University of Alaska	Nicholas Copernicus University

Dept. of Atmospheric Sciences	Geophysical Institute	Inst. Of Geography, Dept. of

AK-40	903 Koyukuk Ave.	ul. Danielewskiego 6

Seattle, WA  98195	Fairbanks, AK  99701	87-100 Torun

POLAND

Dr. Anthony Worby	World Data Center-A	World Data Center-A

GPO Box 252-80	Glaciology (Snow and Ice)	Marine Geology & Geophysics

Hobart, Tasmania 7001	CIRES/University of Colorado	NOAA, E/GC3

AUSTRALIA	Boulder, CO  80309	325 Broadway

Boulder, CO  80303

World Data Center-A: Meteorology	World Data Center-A: Oceanography	Steven Worley  (2)

NOAA, E/CC	NOAA, E/OC53	NCAR/SCD

Federal Building	Silver Spring, MD 20910-3282	P.O. Box 3000

Asheville, NC  28801	Boulder, CO 80307

Mrs. Xu Pei-Min	Dr.Takashi Yamanouchi	Hengchun Ye

Polar Information Data Center	National Instit. of  Polar Research	California State University, Los

Polar Res. Institute of China	1-9-10 Kaga, Itabashi-ku	Dept. of Geography and Urban

Jinqiao Road, Pudong 451	Tokyo, 173-8515	Los Angeles, CA  90032-8222

Shanghai 200129	JAPAN

CHINA

Zhang Yinsheng	Dr. I.A. Zotikov	Dr. H.J. Zwally

Cold And Arid Regions	USSR Academy of Sciences	NASA/Goddard Space Flight Center

Environ. and Engineering Res. 	Institute of Geography	Code 971

Academia Sinica	29 Staromonetny	Greenbelt, MD  20771

Lanzhou 730000	Moscow, 10917

CHINA	RUSSIA